## Slide 1: Lecture 12: Placement – II
Tsung-Wei (TW) Huang
Department of Electrical and Computer Engineering
University of Utah, Salt Lake City, UT

## Slide 2: Recap: Placement Problem
What does a placer do?
  Input: Netlist of gates & nets
  Output: Exact location of each gate
  Goal: Able to route (connect) all wires
Placement is VERY HARD!
  Bad placement  Much more wire
  More wire: bigger, slower chip
  If placement is very bad, next tool in the flow—the router—unable to connect all wires, or meet timing

## Slide 3: Recap: Placement Problem (cont’d)
Grid-based model of the chip
  A simple grid – like a chess board
  Cells (gates) go in grid slots
  Pins (connect off-chip, fixed at edges)
Grid-based model of gates
  All gates are exactly the same size.
  (Unrealistic, but simplifies things)
  Each grid slot can hold 1 gate
Any gate can go in any slot

## Slide 4: Recap: Placement Problem (cont’d)
Placer optimizes the ability of router to connect all the nets
  But routers are computationally expensive tools. We can’t run one “inside” placer
  We need a simplified approximation at this stage
Every real placer minimizes expected wirelength
  For each wire in the design, estimate the expected length of the routed wire
  Minimize this objective: ∑wires Wi EstimatedLength(Wi)
Placer finds gate locations to minimize this objective

## Slide 5: Recap: Wirelength Estimation
Most placers adopt Half-Perimeter Wirelength (HPWL)
  Also know as Bounding Box (BBOX) wirelength
  Put smallest “bounding” box around all gates
  Assume gate lives in “center” of the grid slot
  Add width (∆X) and height (∆Y) of the BBOX for the wirelength estimate
x=0 1 2 3 4
y=5
4
3
2
1
0
x=0 1 2 3 4
y=5
4
3
2
1
0
A “4-point net”
∆X=3-1=2; ∆Y=4-1=3. HPWL=5
∆X=4-1=3; ∆Y=5-1=4. HPWL=7
A “2-point net”

## Slide 6: Recap: Wirelength Estimation (cont’d)
Easy to calculate, even for a multi-point net:
[max{X coordinates of all gates) – min{X coordinates of all gates}] + [max{Y coordinates of all gates) – min{Y coordinates of all gates}]
Always a lower bound on the real wire length
  No matter how complex the final routed wire path is…
  …you need at least this much wire to connect everything
  Aside: all wiring on big chips (and most boards) is strictly horizontal & vertical – no “arbitrary angles” for manufacturing reasons which is another reason HPWL is good

## Slide 7: Recap: Placement Algorithm
# random gate swaps
L = ∑nets Ni HPWL(Ni)
0.1
1
10
100
1000
40K
60K
80K
100K
∑HPWL
20K
T
 Placer progress
Iterative Placer
(fast but bad quality)
SA-based placer
(good quality but slow)

## Slide 8: Analytical Placer
Write an equation whose minimum is the placement
  If you have a million gates, need a million (xi, yi) values as result
  Formulate an appropriate cost function for all the gate-level (xi, yi): F( x1, x2, … x1M, y1, y2, … y1M)
  Solve analytically for X*=(x1, x2, … x1M), Y*=(y1, y2, … y1M) to minimize F( )
  The resulting values of X*, Y* give you the placement of all 1M gates
This sounds sort of crazy… but it works great
  All modern placers for big ASICs and SOCs are “analytical”
  Big trick is write the wirelength in mathematically “friendly” form we can optimize

## Slide 9: Key: Optimize Quadratic Wirelength Model
For 2-point net, we optimize squared length of “distance” line between points: (x1-x2)2 + (y1-y2)2
x= 0 1 2 3 4
y=5
4
3
2
1
0
A “2-point net”
Quadratic wirelength
=(3-1)2 + (4-1)2
=13
BUT… what happens if your net has more than 2 points in it?

## Slide 10: What About k-point Net, k>2?
Replace one “real” net with k(k-1)/2 2-point nets and add a new net between every pair of points–called a fully-connected clique model
x= 0 1 2 3 4
y=5
4
3
2
1
0
Clique model
x= 0 1 2 3 4
y=5
4
3
2
1
0
A “k=4-point net”
2
4
k(k-1)/2
=4(4-1)/2
=6 2-point nets
1
3

## Slide 11: What About k-point Net, k>2? (cont’d)
Each new 2-point net is weighted by 1/(k-1)
  Why? 1 net became k(k-1)/2 nets. Need to compensate so we don’t “overestimate”
x= 0 1 2 3 4
y=5
4
3
2
1
0
Clique model
Quadratic estimate:
(1/3)[(4-1)2 + (5-4)2]
+(1/3)[(4-3)2 + (5-1)2]
+(1/3)[(3-1)2 + (4-1)2]
+(1/3)[(3-1)2 + (4-3)2]
+(1/3)[(4-3)2 + (5-3)2]
+(1/3)[(3-3)2 + (3-1)2]
=sum of 6 weighted 2-point lengths
Note also: when k=2, this weight is just (2-1)=1, so no special treatment for common 2-point nets

## Slide 12: Gates as Points
To make the math work out easily, one more simplification:
  Ignore the physical size of all the gate – pretend gates are dimensionless points
  And, we will ignore (for now…) constraint that gates can’t go on top of each other
Sounds strange… Why?
  Allow us to write a very simple, very elegant “equation” for the placement
  Allow us to solve the problem very quickly and effectively

## Slide 13: Easiest to See with Small Example
Chip surface is a rectangle
  X from 0 to 1; Y from 0 to 1
  This it totally arbitrary, btw
2 gate “points”, index 1 and 2
3 nets, each with a weight
  Each net is 2 points to keep manual example small and easy
  Weights are 1, 2, 4 in diagram
2 pads
  Pad = fixed pin (red square) on the edge of the chip. These do not move.
Gate 1
Gate 2
(0,0)
(1,0.5)
1
2
4
(1,1)

## Slide 14: Easy to Write the Quadratic Wirelength
4(x2-1)2 + 4(y2-0.5)2
2(x2-x1)2 + 2(y2-y1)2
1(x1-0)2 + 1(y1-0)2
Gate 1
Gate 2
(0,0)
(1,0.5)
1
2
4
(1,1)
Next step: How do we optimize this equation?

## Slide 15: How Do We Minimize This?
Basic calculus! Differentiate, set derivative to 0, then solve!
  But this is multiple variables? So, we do partial derivatives, set each to 0, solve x and y independently!
Q(X): 4(x2-1)2 + 2(x2-x1)2 + 1(x1-0)2
Q(Y): 4(y2-0.5)2 + 2(y2-y1)2 + 1(y1-0)2
∂Q/∂x2 = 8(x2-1) + 4(x2-x1) + 0
= -4 x1 + 12 x2 - 8 = 0
∂Q/∂x1 = 0 + 4(x2-x1)(-1) + 2(x1)
= 6 x1 – 4 x2 = 0
∂Q/∂y2 = 8(y2-0.5) + 4(y2-y1) + 0
= -4 y1 + 12 y2 - 4 = 0
∂Q/∂y1 = 0 + 4(y2-y1)(-1) + 2(y1)
= 4 y1 – 4 y2 - 8 = 0

## Slide 16: How Do We Minimize This? (cont’d)
These are linear equations! We know how to solve these!
  Two matrix equations: Ax=bx and Ay=by  N gates gives NxN matrix
  Same matrix for X,Y, different b vectors  X, Y, b are Nx1 vectors
Q(X): 4(x2-1)2 + 2(x2-x1)2 + 1(x1-0)2
Q(Y): 4(y2-0.5)2 + 2(y2-y1)2 + 1(y1-0)2
6 -4
-4 12
x1
x2
=
0
8
6 -4
-4 12
y1
y2
=
0
4
x1 = 0.571 x2 =0.857
y1 = 0.286 y2 =0.429
Minimize
Minimize

## Slide 17: Placement Result
Observation: placement result makes visual sense!
  All points on a straight line between the pads
  Each 2-point wire is like a spring–placement minimizes all spring lengths
Bigger weight on the wire  shorter wire. Gives us lots of control over placement
Same matrix, different right-hand-side b vectors. Why? Different x, y pad coordinates
1
2
(0,0)
(1,0.5)
1
2
4
(1,1)
(0,0)
(1,0.5)
(1,1)
x1 = 0.571 x2 =0.857
y1 = 0.286 y2 =0.429
1
2
4
2
1

## Slide 18: What is Matrix A? (cont’d)
Surprisingly simple recipe to build the required A matrix
  First, build the NxN connectivity matrix, called C
  If gate i has a 2-point wire to gate j with weight w, c[i,j] = w, else = 0
Another example of 3 gates, 3 wires, and 1 I/O pad (P)
1
2
1
3
4
C =
0 1 0
1 0 4
0 4 0
P
5
Note: C matrix ignores the pads

## Slide 19: What is Matrix A?
Use the connectivity C matrix to build A matrix
  Elements a[i,j] not on the matrix diagonal are just a[i,j] = -c[i,j]
  Elements on the diagonal are a[i,j]= ∑j=1,n c[i,j] + (weight of any pad wire)
    …ie, add up the ith row of C and then add in weight on a (possible) wire to pad
C =
1
2
1
3
4
0 1 0
1 0 4
0 4 0
A =
6 -1 0
-1 5 -4
0 -4 4
P
5
diagonal
Note: A matrix accounts for pads

## Slide 20: What is Vector b?
For Ax = bx vector:
  If gate i connects to a pad at (xi, yi) with a wire with weight wi
  Then set bx[i] = wi • xi
For Ay = by vector:
  If gate i connects to a pad at (xi, yi) with a wire with weight wi
  Then set by[i] = wi • yi
A
x
=
bx
ith element of bx vector
(xi,yi)
i
wi
ith element of by vector
A
y
=
by

## Slide 21: How to Solve Ax=b?
Are these difficult to do, in practice?
  If we have 1M gates, this is a 1M x 1M A matrix, with 1M element x and b vectors!
No – these are VERY EASY to solve, even when very large
  The A matrix has a special form—it is sparse, symmetric, diagonally dominant
  Mathematically: A is positive semi-definite—very simple to solve!
  We use iterative, approximate solvers, in practice (i.e., not Gaussian elimination but techniques like conjugate gradient)
    This means the solver converges gradually to the right answer
    But, also means that the answers can be a little bit “off”, not quite perfect

## Slide 22: Another Example
1
2
3
4
(1,0)
(0, 1)
(0.5,0)
5
(1,1)
C =
0 1 10 0 0
1 0 1 1 1
10 1 0 1 0
0 1 1 0 1
0 1 0 1 0
All wire weights = 1 except two highlighted:
gate1 to pad and gate1 to gate2
Weight=10
Weight=10
A =
21 -1 -10 0 0
-1 4 -1 -1 -1
-10 -1 13 -1 0
0 -1 -1 4 -1
0 -1 0 -1 3
bx = 0
0
1
1
0.5
by = 10
0
0
1
0

## Slide 23: Another Example: Result

## Slide 24: Summary
We have discussed a new analytical placement algorithm
We have discussed the quadratic wirelength model
  Construct the matrix A (NxN) for a placement problem of N gates
  Construct the vector bx and the vector by
  Formulate the placement problem into a linear system
  Solve the linear system and get the gate locations
We will dive into the quadratic placement problem next