## Slide 1: Lecture 1: Introduction to Physical Design
Tsung-Wei (TW) Huang
Department of Electrical and Computer Engineering
University of Utah, Salt Lake City, UT

## Slide 2: Logistics
Instructor: Dr. Tsung-Wei Huang (TW)
  tsung-wei.huang@utah.edu
  MEB 2124
Time: MoWe / 3 PM – 4:20 PM (excluding holidays)
  In person: WEB L114
  Zoom (back-up plan): https://utah.zoom.us/j/2468214418
Webpage
  GitHub: https://github.com/tsung-wei-huang/ece5960-physical-design/
Office hour: by appointment

## Slide 3: Scoring
Total 100 points
  Four programming assignments of key physical design algorithms
  Class presentation for each programming assignment
Academic integrity
  I trust you but don’t take it for granted (it’s your career not mine…)
  https://regulations.utah.edu/academics/6-400.php
Textbook
  No need to buy any textbook
  Slides will be available and are enough

## Slide 4: Class Philosophy
Learn important physical design algorithms
  Combinatorial optimization problems (e.g., graph, discrete math)
  Analytical methods (e.g., linear programming)
Program important physical design algorithms
  Write C/C++/Python code to solve physical design problems
  Implement various data structures and algorithms
At the end of the class, I want you to
  Understand important computer design problems
  Improve your coding skills and algorithm knowledge
  Have more job opportunities in software companies (high pay today!)

## Slide 5: Programming Machines
Linux programming environment
  Utah CADE Linux machine: https://www.cade.utah.edu/
  Your personal MacBook, Linux desktop, etc.
Evaluation environment
  Instructor’s server: twhuang-server-01.ece.utah.edu
  Email the instructor (tsung-wei.huang@utah.edu) for an account with
    Your account name
    Your default password
Programming languages
  No restriction but highly recommend C/C++

## Slide 6: Why Programming…?

## Slide 7: What Language?

## Slide 8: From my 10-year Programming Perspective
In general, your logic thinking matters the most
  How to formulate a problem computationally?
  How to solve a computational problem efficiently?
  How to improve the solution quality programmatically?
However, as a CE/CS student, I highly recommend
  C/C++ let you know how performance works
  Python let you know how productivity works
  Java let you know how portability works

## Slide 9: Silicon Compiler (Design Automation)
Logic synthesis
Hardware description (Verilog/VHDL)
Layout (GDSII)
Physical design
Front end
Netlist (gate-level description)
Back end

## Slide 10: Why Silicon Compiler?
Intel 4004 (‘71)
Intel 8080
Intel 8085
Intel 8286
Intel 8486

## Slide 11: Silicon Compiler: Front-end
System Specification
Functional Design
Logic Design
Circuit Design
X=(AB*CD)+(A+D)+(A(B+C))
Y=(A(B+C))+AC+D+A(BC+D))

## Slide 12: Silicon Compiler: Back-end
Physical Design
Fabrication
Packaging

## Slide 13: Physical Design Flow
Large amount of research opportunities!

## Slide 14: Complexity of Physical Design
More than 100 million transistors
Performance driven designs
Power-constrained designs
Time-to-Market
Design cycle
High performance, high cost
……

## Slide 15: History of Physical Design
Born in early 60’s (board layout)
Passed teenage in 70’s (standard cell place and route)
Entered early adulthood in 80’s (over-the-cell routing)
Declared dead in late 80’s !!!
Found alive and kicking in 90’s
Physical Design has become a key force in design cycle
  Thanks to the deep submicron scaling! We really need automation!
  Thanks to algorithm innovations in computer science
  Thanks to computer hardware advancement

## Slide 16: Circuit Partition Example
Which partition result is better?

## Slide 17: Floorplan Example
Many macros
Data paths + logic elements
I/O constraints
  Area
  Wire bond
  Connection (e.g., gate 1 links gate 2)
  …

## Slide 18: Placement Example
Which placement result is better?

## Slide 19: Placement Example (cont’d)
Commercial tools are still away from optimal solutions …

## Slide 20: Lithography Example

## Slide 21: Lithography Example (cont’d)

## Slide 22: Optical Proximity Correction (OPC)
More OPC friendly

## Slide 23: We Need Algorithms!
To optimize design among different objectives, area, power, performance, and etc.
Fundamental questions: How to do it smartly?
Definition of algorithm in a board sense: A step-by-step procedure for solving a problem. Examples:
  Cooking a dish
  Making a phone call
  Sorting a hand of cards
Definition for computational problem
  A well-defined computational procedure that takes some value as input and produces some value as output

## Slide 24: Computational Problems
Decision problem
  Given a positive integer n, determine if n is prime
Search problem
  Find all even numbers in X=[1,2,3,4,5]
Counting problem
  Given a positive integer n, count its number of nontrivial prime factors
Optimization problem
  Given a graph G, find an independent set of G of maximum size
…
How do we solve these problems smartly?

## Slide 25: Example: Big Mod Problem
Computational problem description
  Input: a, b, c (3<a, c<5000000, 1<b<2147483647)
  Output: x = ab (mod c)
A simple solution
  for(i=1, x=1; i<=b; i++)
  x = (x*a)%c;
  std::cout << “a^b % c = ” << x << std::endl;
Is the solution smart enough?

## Slide 26: Example: Big Mod Problem
Computational problem description
  Input: a, b, c (3<a, c<5000000, 1<b<2147483647)
  Output: x = ab (mod c)
A simple solution
  for(i=1, x=1; i<=b; i++)
  x = (x*a)%c;
  std::cout << “a^b % c = ” << x << std::endl;
Is the solution smart enough?
  We need a total of “b” iterations
  Very slow execution for large b

## Slide 27: Refined Solution (Recursive)
#define SQUARE(x) (x*x)
int bigmod(int a, int b, int c) {
if(b==0) return 1;
else if(b%2==0)
return SQUARE(bigmod(a,b/2,c)%c)%c;
else return ((a%c)*bigmod(a,b-1,c))%c;
}
int main() {
int a,b,c;
while(std::cin >> a >> b >> c) std::cout<<bigmod(a,b,c)<<endl;
return 0;
}
  216 = ( 28 )2 total 1 calculation
  28 = ( 24 )2 total 1 calculation
  24 = ( 22 )2 total 1 calculation
  22 = ( 21 )2 total 1 calculation
  21 = ( 20 ) total 1 calculation

## Slide 28: Refined Solution (Iterative)
int bigmod(int a, int b, int c) {
int result = 1;
while(b > 0) {
if(b & 1) {
result = (result * a) % c;
}
b = b >> 1;
a = a*a%c;
}
return result;
}

## Slide 29: Runtime Comparison
https://www.onlinegdb.com/
Runtime (with –O2) – Enabled Optimization |  |  | 
(a, b, c) | Naive | Refined (recursive) | Refined (iterative)
(2, 1000000, 3) | 13720 us | 24 us | 22 us
(2, 10000000, 3) | 136148 us | 9 us | 4 us
(2, 100000000, 3) | 1320049 us | 8 us | 4 us

## Slide 30: Code Analysis
https://godbolt.org/z/6zT4cK3Wz
 | Naive | Refined (recursive) | Refined (iterative)
Lines of C++ Code | 7 | 11 | 11
Lines of Assembly (-O0) | 55 | 99 | 59
Lines of Assembly (-O2) | 27 | 57 | 32

## Slide 31: Magic behind the Refined Solution
In fact, there is a name for the refined method:
Divide and Conquer (D&C) algorithm
(used to solve >50% large and complex computational problems, e.g., Google Map, sorting, etc.)

## Slide 32: D&C is Widely used in Physical Design
Modern circuits sizes are too large to handle in a flat fashion
42M transistors
1.5MHz; 224 mm2
Directly solving the original problem takes forever to finish …
Notes: Like I said, Divide and Conquer is heavily used in CAD. Modern circuit sizes are just too large to handle in flat. If you do this, it means billions of transistors at one time. You have no hope to finish it in a reaonsable amount of time. To give you a sense on the size, when I was working in IBM ....( explore )

## Slide 33: Example: D&C-based Placement
Notes: Let's take a look at one step of computer design, placement. A placement is a step that tries to find the location of each gate, you know Or gate, NAND gate, NOT gate, and other gates, in a chip area. And we have billions of gate to place in a finger size chip.
Computer design tools don't do this. They do this in divide and conquer. (explain)

## Slide 34: Example: D&C-based Placement

## Slide 35: Example: D&C-based Placement

## Slide 36: Example: D&C-based Placement

## Slide 37: Example: D&C-based Placement

## Slide 38: Example: D&C-based Placement

## Slide 39: Example: D&C-based Placement

## Slide 40: Example: D&C-based Placement
Notes: So, from iteration to iteration you can clearly see cells are placed very regularly, right, Cells are spreading along the 2D grid partition. We partition the large chip care into smaller grids and place cells in those small grids. Solving the smaller grid problem is definitely more efficiently than directly handling the original problem.

## Slide 41: Summary
We have discussed class logistics
We have discussed design automation flow
We have discussed physical design
We have discussed concept of computational problems
We have discussed a computational problem example
  Problem formulation
  Naïve solution
  Refined solution
  Practical code analysis techniques