## Slide 1: Lecture 11: Placement – I
Tsung-Wei (TW) Huang
Department of Electrical and Computer Engineering
University of Utah, Salt Lake City, UT

## Slide 2: Physical Design Flow

## Slide 3: Placement
Places a netlist of gates and wires in a chip
  Min wirelength
  Min area
  Min power
  Min delay
  …

## Slide 4: Example
Which placement result is better?

## Slide 5: Placement Problem
What does a placer do?
  Input: Netlist of gates & nets
  Output: Exact location of each gate
  Goal: Able to route (connect) all wires
Placement is VERY HARD!
  Bad placement  Much more wire
  More wire: bigger, slower chip
  If placement is very bad, next tool in the flow—the router—unable to connect all wires, or meet timing

## Slide 6: Analogy to City Planning
How to plan a city for 5-10M+ people?

## Slide 7: Requirement for Placement
Must handle 4-10M cells, 1000s macros
  64 bits + near-linear asymptotic complexity
Accept fixed ports/pads/pins + fixed cells
Place macros, esp. with var. aspect ratios
  Non-trivial heights and widths (ex: height=2rows)
Honor targets and limits for net length
Respect floorplan constraints
Handle a wide range of placement densities
  From <25% to 100% occupied

## Slide 8: Requirement for Placement (cont’d)
Add / delete filler cells and Nwell contacts
Ignore clock connections
ECO (Engineering Change Order) placement
  Fix overlaps after logic restructuring
  Place a small number of unplaced blocks
Datapath planning services
  Ex: many-core processor units
Provide dialog services to enable cooperation across tools
  Ex: between placement and synthesis

## Slide 9: Importance of Placement
Placement is a fundamental problem for physical design
Becomes very active again in recent years:
  Many new academic placers since 2000
  Many other publications to handle timing, routability, etc.
Reasons:
  Serious interconnect issues (delay, routability, etc.) in advanced nodes
    Placement determines interconnect to the first order
    Need placement information even in early design stages (ex: logic synthesis)
  Placement problem becomes significantly larger
  Cong et al. [ASPDAC-03, ISPD-03, ICCAD-03] point out that existing placers are far from optimal, not scalable, and not stable

## Slide 10: Industry-Academia Collaboration

## Slide 11: Placement for Different Design Styles
Standard cell placement (main focus of this course!)
Gate array / FPGA placement
Macro block placement
  Typically called floorplanning
Mixed-size placement
  A few large macro blocks
  A large number of small cells
Wafer-scale placement
  Thousands of processor units
Wafer-scale placement:
https://github.com/Cerebras/ispd2021

## Slide 12: Placement in Machine Learning
GPU device placement optimization for neural networks
Place each tensor operator onto a GPU for improved performance
https://arxiv.org/abs/1706.04972

## Slide 13: Placement Footprints
Standard Cell
Data Path
IP - Floorplanning

## Slide 14: Placement Footprints (cont’d)
Core
Control
IO
Reserved areas
Mixed data path & sea of gates

## Slide 15: Placement Footprints
Perimeter IO
Area IO

## Slide 16: Commercial Tools

## Slide 17: Placement is VERY HARD
Even this simplified placement problem is NP-complete
  1D placement
  2-pin nets only
  All modules are of the same size
  Wirelength as the only cost function
Realistic placement problems are
  2D placement
  Multi-pin nets
  Modules of different sizes
  Various cost function in addition to total wirelength
  Various constraints for different target applications
bad placement
good placement

## Slide 18: Let’s Start with a Simple Placer
Very simple model of the chip
  A simple grid – like a chess board
  Cells (gates) go in grid slots
  Pins (connect off-chip, fixed at edges)
Very simple model of gates
  All gates are exactly the same size.
  (Unrealistic, but simplifies things)
  Each grid slot can hold 1 gate
Any gate can go in any slot

## Slide 19: Objective of a Placer
Placer optimizes the ability of router to connect all the nets
  But routers are computationally expensive tools. We can’t run one “inside” placer
  We need a simplified approximation at this stage
Every real placer minimizes expected wirelength
  For each wire in the design, estimate the expected length of the routed wire
  Minimize this objective: ∑wires Wi EstimatedLength(Wi)
Placer finds gate locations to minimize this objective

## Slide 20: Placement Terminology
Common term for a wire in a layout is called Net
  The whole set of gates and wires is called netlist
  Net categorized by how many things it connects.
A “2-point net”
x= 0 1 2 3 4
y=5
4
3
2
1
0
A “4-point net”
y=5
4
3
2
1
0
x= 0 1 2 3 4

## Slide 21: Wirelength Estimation
Many different estimators for different placer methods
  Multi-point nets can be routed in many different paths
  In a dense layout, nets do not all get routed in a “shortest path”
x=0 1 2 3 4
y=5
4
3
2
1
0
x= 0 1 2 3 4
x=0 1 2 3 4
y=5
4
3
2
1
0
y=5
4
3
2
1
0

## Slide 22: Half-perimeter Wirelength (HPWL)
Most placers adopt Half-Perimeter Wirelength (HPWL)
  Also know as Bounding Box (BBOX) wirelength
  Put smallest “bounding” box around all gates
  Assume gate lives in “center” of the grid slot
  Add width (∆X) and height (∆Y) of the BBOX for the wirelength estimate
x=0 1 2 3 4
y=5
4
3
2
1
0
x=0 1 2 3 4
y=5
4
3
2
1
0
A “4-point net”
∆X=3-1=2; ∆Y=4-1=3. HPWL=5
∆X=4-1=3; ∆Y=5-1=4. HPWL=7
A “2-point net”

## Slide 23: About HPWL
Easy to calculate, even for a multi-point net:
[max{X coordinates of all gates) – min{X coordinates of all gates}] + [max{Y coordinates of all gates) – min{Y coordinates of all gates}]
Always a lower bound on the real wire length
  No matter how complex the final routed wire path is…
  …you need at least this much wire to connect everything
  Aside: all wiring on big chips (and most boards) is strictly horizontal & vertical – no “arbitrary angles” for manufacturing reasons which is another reason HPWL is good

## Slide 24: About HPWL (cont’d)
Real distribution of HPWL for 200K gate IBM ASIC [DAC97]
  181K nets. Note LOG scale. Most nets are short. But there is a long tail to distribution.
Number of nets
Chart: 
| 0.0-0.5 | 0.5-1.0 | 1.0-1.5 | 1.5-2.0 | 2.0-2.5 | 2.5-3.0 | 3.0-3.5 | 3.5-4.0 | 4.0-4.5 | 4.5-5.0 | 5.0-6.0 | 6.0-7.0 | 7.0-8.0 | 8.0-9.0 | 9.0-10.0 | 10.0-15.0 | 15.0-20.0
 | 129624 | 22292 | 8980 | 5999 | 4127 | 2877 | 2050 | 1456 | 1086 | 706 | 933 | 396 | 162 | 64 | 28 | 60 | 6
HPWL

## Slide 25: A Simple Iterative Placer
Start with a random placement
  Just randomly assign each gate to a grid location (1 gate per entry)
  Yes – this is a terrible placement. Really big L = ∑nets Ni HPWL(Ni)
Random iterative improvement
  Pick a random pair of gates in the grid and swap their locations
  Evaluate the change in
    L = ∑nets Ni HPWL(Ni);
    ΔL= [new HPWL – old HPWL]
  If ΔL<0, new L got smaller  Improvement! Keep this swap
  If ΔL>0, new L got bigger  Worse! Undo this swap
  Keep doing this for many, many random swaps, until L stops improving

## Slide 26: A Simple Iterative Placer: Pseudocode
foreach( gate Gi in netlist ) //random initial placement
place Gi in random location (x,y) in grid not already occupied
L=0 //calculate initial HPWL wirelength for whole netlist
foreach( net Ni in the netlist )
L = L + HPWL(Ni);
while ( overall HPWL wirelength L is improving ) { //main improvement loop
pick random gate Gi; pick random gate Gj;
swap gates Gi and Gj
evaluate ΔL = new HPWL - old HPWL;
if ( ΔL < 0 ) { // improved placement! Update HPWL
L = L + ΔL
else // ΔL > 0, this is a worse placement
undo swap of Gi and Gj
}

## Slide 27: Computing ΔL Efficiently (Incrementally)
Incremental wirelength update calculation
  Cannot afford to re-compute length of each net in entire placement after each swap! – most nets did not change
  Compute ΔL incrementally – just look at nets that could change
ΔL = [ HPWL(i) + HPWL(j) + HPWL(k) after swap] - [ HPWL(i) + HPWM(j) + HPWL(k) before swap]
x=0 1 2 3 4
y=5
4
3
2
1
0
1
2
Swap
Gates 1,2
Net i
Net j
Net k
x=0 1 2 3 4
y=5
4
3
2
1
0
1
2
Net i
Net j
Net k

## Slide 28: How does this Simple Placer Work?
It works ok …
  Small benchmark
  ~2500 gates + ~500 pins
  Placed in a 50x50 grid
Graph shows progress
  Y axis: L = ∑nets Ni HPWL(Ni)
  X axis: # swaps
  Yes, this ran for 8M swaps until progress on L stopped
# random gate swaps
L = ∑nets Ni HPWL(Ni)

## Slide 29: Takeaways for the Simple Placer
Easy to understand and to implement
  Start with a random placement and randomly improve the wirelength until it stops getting better
  Can optimize what we care about: estimated wirelength ∑nets Ni HPWL(Ni)
  It will improve at each iteration always
However, the final result is still not very good
  We are being too greedy to go out of the local optimal
We can do better for sure

## Slide 30: Problem of the Simple Placer?
Imagine you could plot ∑HPWL for all possible placements
  Our random method only takes swaps that improve wirelength
  Can only find good results downhill from our random start
∑HPWL
(lower is better)
All possible placement solutions we could find
Easy to get stuck in a local minimum
If there are better answers, how to find?

## Slide 31: Downhill and Uphill Movement
If we could go uphill, we may get better placements
  How to control this?
All possible placement solutions we could find
∑HPWL
(lower is better)

## Slide 32: Simulated Annealing (SA)-based Placer
Start with a random initial placement with wirelength = ∑HPWL(net)
T = temperature = hot; frozen = false;
while ( ! frozen ) {
for (s=1; s< M* #gates in layout; s++) { // M is how many swaps-per-gate
Swap 2 random gates Gi and Gj
Compute ∆L = [∑HPWL(net) before swap] - [∑HPWL(net) after swap]
if (∆L < 0 )
then accept this swap //this is a new, better placement
else {
if( uniform_random() < exp( -∆L/T ) )
then accept this ‘uphill’ swap //this is a new, worse placement
else undo this ‘uphill’ swap
}
if (∑HPWL(net) still decreasing over the last few temperatures)
then T = 0.9 * T // cool the temperature; do more gate swaps
else frozen = true
}
return (final placement as best solution)
New: Probabilistic swap accept
Annealing temperature cooling “outer loop”

## Slide 33: Neighboring Solutions
M3: Change the orientation of a macro, if any
1 2
3 4
2 1
3 4
1 2
3 4
Axis of reflections
M1: Displace a module to a new location
M2: Swap two gates
.
.

## Slide 34: Move Selection Strategy
Select a move between M1 and M2
  Prob(M1)=4/5
  Prob(M2)=1/5
If a move of type M1 is chosen and is rejected
  Take a move of type M3 (for the same gate) with probability 1/10
Restriction on
  How far a module can be displaced
  What pairs of modules can be interchanged
M1: Displacement
M2: Interchange
M3: Reflection

## Slide 35: Move Restriction
Range Limiter
  At the beginning, R is very large, big enough to contain the whole chip
  Window size shrinks slowly as the temperature decreases. In fact, height and width of R  log(T)
  Switching move begins when window size are so small that no inter-row modules interchange is permitted
Rectangular window R

## Slide 36: How does an SA-based Placer Work?
It works better
  Same 2500 gate benchmark
  HOT=800, M=100 moves/gate
  About 30% less HPWL wirelength compared to the simple placer
Typical annealing “cost” curve
  X axis is T=temperature, LOG scale
    Do 100x2500 swaps/temperature
    Read right-to-left
  Y axis is ∑HPWL, but LOG scale
  Cool fact: curves always look like this!
0.1
1
10
100
1000
40K
60K
80K
100K
∑HPWL
120K
20K
T
 Placer progress

## Slide 37: Problem of SA-based Placer
Simulated annealing is a very successful method
  Much better than dumb random improvement
  Dominant method for placers in 1980s, 1990s
  And still today – used in lots of other VLSI CAD tasks (e.g., portioning, floorplanning, etc.)
However, this is not not how we really do placers today
  Annealing works well for up to 100K – 500K gates
  Annealing too inefficient for things with 1M+ gates
    Today’s designs can easily have 500M+ gates
We need another new set of ideas

## Slide 38: A Famous SA-based Placer: TimberWolf
http://www.twolf.com/
“The Timberwolf Placement and Routing Package”, Sechen, Sangiovanni; IEEE Journal of Solid-State Circuits, vol SC-20, No. 2(1985) 510-522

## Slide 39: Summary
We have discussed basic ideas of placement
We have discussed importance and difficulty of placement
We have discussed the problem formulation of placement
  Terminology
  Input, output, objective
  Wirelength estimation
We have discussed two simple placement solutions
  Random iterative improvement-based placement algorithm
  Simulated annealing-based placement