## Slide 1: Lecture 13: Placement – III
Tsung-Wei (TW) Huang
Department of Electrical and Computer Engineering
University of Utah, Salt Lake City, UT

## Slide 2: Recap: Analytical Placer
Write an equation whose minimum is the placement
  If you have a million gates, need a million (xi, yi) values as result
  Formulate an appropriate cost function for all the gate-level (xi, yi): F( x1, x2, … x1M, y1, y2, … y1M)
  Solve analytically for X*=(x1, x2, … x1M), Y*=(y1, y2, … y1M) to minimize F( )
  The resulting values of X*, Y* give you the placement of all 1M gates
This sounds sort of crazy… but it works great
  All modern placers for big ASICs and SOCs are “analytical”
  Big trick is write the wirelength in mathematically “friendly” form we can optimize

## Slide 3: Recap: Quadratic Wirelength Model
We optimize squared length of “distance” line between points: (x1-x2)2 + (y1-y2)2
x= 0 1 2 3 4
y=5
4
3
2
1
0
A “2-point net”
Quadratic wirelength
=(3-1)2 + (4-1)2
=13
For k-point net, we use the clique model (complete graph for each net)

## Slide 4: Recap: Quadratic Placement Formulation
1
2
3
4
(1,0)
(0, 1)
(0.5,0)
5
(1,1)
C =
0 1 10 0 0
1 0 1 1 1
10 1 0 1 0
0 1 1 0 1
0 1 0 1 0
All wire weights = 1 except two highlighted:
gate1 to pad and gate1 to gate2
Weight=10
Weight=10
A =
21 -1 -10 0 0
-1 4 -1 -1 -1
-10 -1 13 -1 0
0 -1 -1 4 -1
0 -1 0 -1 3
bx = 0
0
1
1
0.5
by = 10
0
0
1
0

## Slide 5: Recap: Quadratic Placement Result
Placement  Solving a linear system

## Slide 6: Summary
We have discussed a new analytical placement algorithm
We have discussed the quadratic wirelength model
  Construct the matrix A (NxN) for a placement problem of N gates
  Construct the vector bx and the vector by
  Formulate the placement problem into a linear system
  Solve the linear system and get the gate locations
We will dive into the quadratic placement problem next

## Slide 7: How does Quadratic Placement Look?
Like the right figure:
  Small IBM ASIC, few thousand gates
  All lumped together to give the minimum wirelength
New problem:
  Quadratic model minimizes wirelength for big netlists, in a numerical way
  But ignores that gates have physical size, cannot be on top of each other
  Now, we have to fix this…
  Our solution: recursive partitioning

## Slide 8: A Bigger Industrial Example
This benchmark is from IBM
  210,904 gates (blue)
  543 fixed blocks (red) –like SRAMS
  Image shows where gates “want” to go if we model blocks like “big pads”
  This is a quadratic placement of gates
  Additional problems: gates need to go between these blocks!
Why we are showing this?
  Example of how badly imbalanced the quadratic placement can be

## Slide 9: Recursive Partitioning
1st quadratic place (QP) solve
Just keep going
Partition chip into left / right. Select which gates on each side.
Solve 2 new, smaller QP tasks
Repeat. Partition each side top/bottom.
Solve 4 new smaller QP solves

## Slide 10: Example: Partition-based Placement
Notes: Let's take a look at one step of computer design, placement. A placement is a step that tries to find the location of each gate, you know Or gate, NAND gate, NOT gate, and other gates, in a chip area. And we have billions of gate to place in a finger size chip.
Computer design tools don't do this. They do this in divide and conquer. (explain)

## Slide 11: Example: Partition-based Placement

## Slide 12: Example: Partition-based Placement

## Slide 13: Example: Partition-based Placement

## Slide 14: Example: Partition-based Placement

## Slide 15: Example: Partition-based Placement

## Slide 16: Example: Partition-based Placement

## Slide 17: Example: Partition-based Placement
Notes: So, from iteration to iteration you can clearly see cells are placed very regularly, right, Cells are spreading along the 2D grid partition. We partition the large chip care into smaller grids and place cells in those small grids. Solving the smaller grid problem is definitely more efficiently than directly handling the original problem.

## Slide 18: Quadratic Legalization: Basic Idea
Partition
  How do we divide the chip into new, smaller placement tasks?
Assignment
  Which gates should go into each new, smaller region?
Containment
  Formulate new linear system matrix solves so gates stay in new regions, with short wirelength
Discuss one early strategy from a classical paper
  Ren Song Tsay, Ernest Kuh, Chi Ping Hsu, “PROUD: A Sea-Of-gates Placement Algorithm,” IEEE Design & Test of Computers, Dec 1988.

## Slide 19: Recursive Partition
After 1st quadratic placement (QP), divide chip area exactly in half, vertically (horizontal is ok too)
We want half the gates on each side

## Slide 20: Recursive Partitioning: How to Assign?
What if QP does not spread gates evenly between halves?
How do we know which gates to put left vs right if this is initial QP?
We partition region at exact center. How do we reformulate a new QP to re-do the gates on each side?

## Slide 21: Recursive Partitioning: How to Assign?
Sort placed gates on X coordinate, then Y (for horizontal cut – sort on Y first, then X); If N total gates, then first N/2 in sorted list go on left; others on right
Sorted on X coordinate, these are left-most N/2 of N gates
This sorting assigns which gates go left, and go right

## Slide 22: Recursive Partitioning: How to Assign?
Focus on the gates inside this shaded region R on the left side of the cut.
R
New big questions:
(1) How do we keep the gates assigned to left side actually in the left side?
(2) How do we model wires that connect to gates/pads on right? Can’t ignore these!
R

## Slide 23: Recursive Partitioning: How to Contain?
Idea: Pseudo-pads
  Every gate & pad not inside region R is modeled as a pad on boundary of R
  Propagate these outside gates using their current (x,y) location to nearest point on R;
  For this example, we take the y coordinate, and put pad on center of cut line x
Solution: model gates/pads on right as “fake” pads on left.
R
Resulting new QP problem for gates in left region
R

## Slide 24: Why this Works?
Cannot ignore gates outside region we are re-placing
  Want gates inside to feel pull from wires to gates outside region
  Pseudo-pads do this for us
Pseudo-pads guarantee all gates re-locate inside region
  Think of wires as ‘springs’ that each pull gates toward other gates or pads
  If pads (real & pseudo) are on edges of region – QP keeps gates inside

## Slide 25: Example
1
2
3
a
b
c
4
5
1. Initial netlist
5 gates (1,2,3,4,5)
8 wires
3 pads (a,b,c)
a
b
c
2. Initial QP
2
3
1
5
4
placed
a
b
c
3. First partition
Sort on X:
Gate order 1 5 4 3 2
Pick: 1 5 4 on left
2
3
1
5
4

## Slide 26: Example (cont’d)
4. Propagate gates/pads
Right-side gates: 2,3
Right-side pads: b
Push to cut, using y coordinates
a
b
c
2
3
1
5
4
2
3
5. 2nd QP input
This is set up for this new smaller placement
a
c
1
5
4
2
3
6. 2nd QP solved
New placement
a
c
1
5
2
placed
3
4
Note: do not propagate pad b, since no wires on left connect to it

## Slide 27: Example (cont’d)
8. Propagate gates/pads
This is set up for next, new smaller placement
a
b
c
2
placed
c
4
5
3
1
5
4
1
7. Left side placed.
Now, re-place right-side gates.
a
b
c
2
3
placed
1
5
4
9. 3nd QP input
This is set up for this new smaller placement
2
b
c
4
5
1
3
b
c
4
5
1
10. 3nd QP solve
placed
2
3

## Slide 28: Example (cont’d)
a
c
placed
b
placed
Repeat: Horizontal
partition on left
2
3
1
5
4
Focus on top. Sort gates on Y
Assign gates 1,5 to region.
a
c
b
2
3
1
5
4
a
c
3
1
5
4
b
placed
2
4
2,3
Propagate gates & pads
Note: do not propagate pad b, no wires to 1,5
Note: gates 2,3 propagate to corner of new region: closest point
Note: gate 4 propagates up to bottom of new region

## Slide 29: Keep Repeating this Recursion
Keep recursively partitioning…
  Usually, you continue until you have a “small” number of gates in each region
  Small >> 1 typically. 10-100 for example
  Get a good, “global” placement, but not a “final” placement
a
c
3
1
5
4
b
placed
2
Continue…
placed
placed
placed

## Slide 30: Final Placement Step: Legalization
Still need to force gates in precise rows for final result
  QP methods cannot force individual gates into standard cell rows, without overlaps
Solution step is called: Legalization
  Many different algorithms. One easy way to do this is by annealing!
  Do local improvement based on swaps of nearby gates
  To anneal, set T=HOT to be very small (cold), so don’t disrupt QP result

## Slide 31: Summary
We have discussed problems of plain quadratic placement
  Gates are easily lumped together to minimize wirelength
We have discussed a solution: partition-based placement
  Partition the placement region iteratively
  Introduce auxiliary pads between partition boundaries
We have discussed legalization
  Remove all overlaps among gates
  Improve wirelength in a local region (e.g., rows)