## Slide 1: Lecture 17: Routing – II
Tsung-Wei (TW) Huang
Department of Electrical and Computer Engineering
University of Utah, Salt Lake City, UT

## Slide 2: Recap: Routing
Notes: So far, we have talked about three important problems in physical design, partition, floorplan and placement. There is one very important step after placement, called clock tree synthesis or CTS, which we may not have enough time to talk about. But the essential idea is very similar to routing, you know, we want to establish connection between placed cells but only for sequential elements.
So, today, we are going to talk about routing. A very important step after placement. This is probably the most difficult part in the entire physical design flow, not just because of its problem difficulty but also its computational complexity.

## Slide 3: Recap: Challenges of Routing
Scale
  Big chips have an enormous number (millions) of wires
  Not every wire gets to take an “easy” path to connect its pins
  Must connect them all--can’t afford to tweak many wires manually
Geometric complexity
  It used to be representing the layout was a simple “grid”
  No longer true: at nanoscale, geometry rules are complex – makes routing hard
Electrical complexity
  It’s not enough to make sure you connect all the wires
  Must ensure delays thru the wires are not too big
  And wire-to-wire interactions (crosstalk) don’t mess up
Notes: Why is routing challenging? First of all, it is the scale. (explain …)
Second, it’s the geometric complexity. (explain …)
Finally, we need to consider electrical complexity.

## Slide 4: Recap: Global and Detailed Routing
N3
N3
N1
N2
N1
N3
N1
N2
N3
N3
N1
N2
N1
N3
N1
N2
Horizontal Segment
Via
Vertical Segment
Detailed Routing
Global Routing
Notes: To overcome these challenges, we typically break down the routing problem into two parts, global routing and detailed routing. (explain global routing)

## Slide 5: Recap: Maze Router
Start at the source
Find all new cells that are reachable
at pathlength 1, ie, all paths that are just 1 unit in total length (just 1 cell) - mark all with this the pathlength
Using the pathlength 1 cells,
find all new cells which are reachable at pathlength 2
Repeat the expansion until the target is found!
S
1
1
2
2
2
2
Notes: We talked about a The key idea behind maze routing is the expansion process. You start at the source node, ok, (click), then you find all … (click) …

## Slide 6: Recap: Maze Router Walkthrough – I
Strategy
  Expand one cell at a time until all the shortest paths from S to T are found.
  Expansion creates a wavefront of paths that search broadly out from source cell until target is hit
  Remember this!? We have done this using breadth-first-search (BFS) algorithm!
S
T
1
2
2
2
2
3
3
3
3
3
3
4
4
4
4
4
4
5
5
5
5
5
5
5
6
6
6
6
6
6
7
7
7
Notes: Let’s walk through the algorithm using a simple. Here I have a 6 by 6 grid that models the routing problem in a 2D layout. Here, I have my source location and my target location. The goal is to establish a shortest route from the source location to the target location.
We know the strategy of maze routing is (explain …)

## Slide 7: Recap: Maze Router Walkthrough – II
S
T
1
2
2
2
2
3
3
3
3
3
3
4
4
4
4
4
4
5
5
5
5
5
5
5
6
6
6
6
6
6
7
7
7
Now what? Backtrace
  Select a shortest-path (any shortest-path) from target back to source
  Mark its cells so they cannot be used again – mark them as obstacles for later wires we want to route
  Since there are many paths back, optimization information can be used to select the best one
  Here, just follow the pathlengths in the cells in descending order
Notes: After we hit the target during the course of the expansion, we can stop since we find a shortest route. Now what? We need to find one path that connects S to T, right? We can do this by backtrace. (explain first item and the figure)

## Slide 8: Recap: Maze Router Walkthrough – III
S
T
Now what? Clean-up
  Clean up the grid for the next net, leaving the S to T path as an obstacle
  Now, ready to route the next net with the obstacles from the previously routed net in place in the grid
Notes: After we decide a path between S and T, we will do a clean-up step. We clean up the grid for the next routing problem by leaving the S to T path as an obstacle. Why? (ask student)
Now, we are ready to route the next net with the obstacles from the previously routed net in place in the grid.

## Slide 9: Recap: Maze Router Walkthrough – IV
S
T
S
T
Also called “Blockages”
  Any cell you cannot use for a wire is a an obstacle or a blockage
  There may be parts of the routing surface you just cannot use
  But most importantly, you label each newly routed net as a blockage
  Thus, all future nets must route around this blockage
Notes: This path marked in black is also called blockages. (explain…)

## Slide 10: Recap: Steiner Tree Constructions
Pins to connect
Route it so we guarantee each 2-point path
is shortest; this is Minimum Spanning Tree
Redraw it--different
orientations
of 2-point paths
Now we can see the
better (shorter)
Steiner tree
2 so-called “Steiner-points”
EASY
HARD!
Notes: This slide shows you an example of steiner tree constructions. Assume we have a four-pin net to route, (click) an easy way is to connect them along the boundary of the enclosed bounding box of the net.
Or, (click), we can have a connection like this
(click) alternatively, we can change the solution in a way that all wires go inside the bounding box while still getting us the optimal wirelength. In this case, we may need to introduce several “bend points” or “turn points”, you know, the location you make a turn. This turn point has a special name called steiner point. Many steiner tree construction algorithms are focusing on finding the steiner points to approximate the optimal solution.

## Slide 11: Channel and Switchbox Routing
A
A
B
B
B
B
B
C
C
C
C
D
D
B
B
E
E
Vertical Channel Tracks
Horizontal Channel Tracks
E
B
D
B
Channel Routing
Notes: In most global routing algorithms, maze routing is applied net by net to decide the route connection among nets, either two-pin net or multi-pin net. Once we have decided the rough connection, the job of detailed routing is to establish the actual connection among nets, and we want to follow the guidance of global routing because we assume a good global routing has tried the best to give us the solution that is hopefully routable.
So, if you look at the routing layout, there are two types of detailed routing, channel and switchbox routing. Channel routing happens at the narrow region between two blocks, while the routing that goes through multiple blocks is called switchbox routing. Of course, channel routing is easier than switchbox routing because we only need to consider the routing between blocks.
We will talk about channel routing in today’s lecture.

## Slide 12: Channel Routing Terminology – I
Power Rail
Channel
External Pad
Standard Cell Row
Notes: Before we start with channel routing, there are some terminology. This is a real channel routing problem from a circuit design. You can see the channel routing happens between rows of standard cells. (explain …)

## Slide 13: Channel Routing Terminology – II
Cell Area
A
A
B
B
B
B
B
C
C
C
C
D
Three-Layer OTC Routing OTC: Over the cell
A
A
B
B
B
B
B
C
C
C
C
D
Two-Layer Channel Routing
Cell Area
Metal3
Via
Metal1
Metal2
Via
Metal1
Metal2
Notes: We often restrict our channel routing to happen in just two layers. Remember we talked about routing layer last time. Typically you have multiple layers to establish your route. Each layer is restricted to either horizontal or vertical direction. For example, at metal 1 you may only go vertically and if you want to go horizontally, you need to go through the upper layer or lower layers.
When that happen, you need to make a turn, right. And the turn is connected through a “Via”, which is a special metal to send signals between layers. So the two layer channel routing looks like this: (explain …)
(Explain the three layer routing…)

## Slide 14: Channel Routing Terminology – III
Columns
Tracks
Channel Height
A
A
B
B
B
B
B
C
C
C
C
D
a
b
c
d
e
f
g
1
2
3
Pin Locations
Horizontal Segment (Trunk)
Vertical Segment (Branch)
0
0
Via
Metal1
Metal2
Notes: Based on the model of two-layer channel routing, we define the following terms:

## Slide 15: Channel Routing Terminology – IV
A horizontal constraint exists between two nets if their horizontal segments overlap
A
A
B
B
C
C
Horizontally unconstrained
Horizontally constrained

## Slide 16: Channel Routing Terminology – V
A vertical constraint exists between two nets if they have pins in the same column: the vertical segment coming from the top must “stop” before overlapping with the vertical segment coming from the bottom in the same column
Vertically constrained with a vertical conflict (route back)
Vertically constrained without conflict (route back)
B
A
A
B
B
A
A
B
B
A
B
A

## Slide 17: Horizontal and Vertical Constraint Graph
The relative positions of nets in a channel routing instance can be modeled by horizontal and vertical constraint graphs
These graphs are used to
  initially predict the minimum number of tracks that are required
  detect potential routing conflicts

## Slide 18: Horizontal and Vertical Constraint Graph
Let S(col) denote the set of nets that pass through column col
S(col) contains all nets that either (1) are connected to a pin in column col or (2) have pin connections to both the left and right of col
Since horizontal segments cannot overlap, each net in S(col) must be assigned to a different track in column col
S(col) represents the lower bound on the number of tracks in colum col; lower bound of the channel height is given by maximum cardinality of any S(col)
A
C
E
C
E
A
F
H
H
G
0
0
B
D
E
B
G
F
0
D
0
0
Column a b c d e f g h i j k
S(b)
= {A, B, C} – lower bound of # tracks = 3

## Slide 19: Horizontal and Vertical Constraint Graph
B
A
C
D
E
F
G
H
A
C
E
C
E
A
F
H
H
G
0
0
B
D
E
B
G
F
0
D
0
0
0
B
D
E
B
G
F
0
D
0
0
Column a b c d e f g h i j k
A
C
E
C
E
A
F
H
H
G
0
a b c d e f g h i j k

## Slide 20: Horizontal and Vertical Constraint Graph
0
B
D
E
B
G
F
0
D
0
0
Column a b c d e f g h i j k
A
C
E
C
E
A
F
H
H
G
0
B
A
C
D
E
F
G
H
A
C
E
C
E
A
F
H
H
G
0
0
B
D
E
B
G
F
0
D
0
0
S(a) = {A}
S(b) = {A,B,C}
S(c) = {A,B,C,D,E}
S(d) = {A,B,C,D,E}
S(e) = {A,B,D,E}
S(f) = {A,D,F}
S(g) = {D,F,G}
S(h) = {D,G,H}
S(i) = {D,G,H}
S(j) = {G,H}
S(k) = {G}
a b c d e f g h i j k

## Slide 21: Horizontal and Vertical Constraint Graph
0
B
D
E
B
G
F
0
D
0
0
Column a b c d e f g h i j k
A
C
E
C
E
A
F
H
H
G
0
B
A
C
D
E
F
G
H
A
C
E
C
E
A
F
H
H
G
0
0
B
D
E
B
G
F
0
D
0
0
S(a) = {A}
S(b) = {A,B,C}
S(c) = {A,B,C,D,E}
S(d) = {A,B,C,D,E}
S(e) = {A,B,D,E}
S(f) = {A,D,F}
S(g) = {D,F,G}
S(h) = {D,G,H}
S(i) = {D,G,H}
S(j) = {G,H}
S(k) = {G}
a b c d e f g h i j k

## Slide 22: Zone Representation: {A}
0
B
D
E
B
G
F
0
D
0
0
Column a b c d e f g h i j k
A
C
E
C
E
A
F
H
H
G
0
B
A
C
D
E
F
G
H
A
C
E
C
E
A
F
H
H
G
0
0
B
D
E
B
G
F
0
D
0
0
S(a) = {A}
S(b) = {A,B,C}
S(c) = {A,B,C,D,E}
S(d) = {A,B,C,D,E}
S(e) = {A,B,D,E}
S(f) = {A,D,F}
S(g) = {D,F,G}
S(h) = {D,G,H}
S(i) = {D,G,H}
S(j) = {G,H}
S(k) = {G}
A
Lower bound on the number of tracks = 5
a b c d e f g h i j k
Zone representation

## Slide 23: Zone Representation: {A, B}
0
B
D
E
B
G
F
0
D
0
0
Column a b c d e f g h i j k
A
C
E
C
E
A
F
H
H
G
0
B
A
C
D
E
F
G
H
A
C
E
C
E
A
F
H
H
G
0
0
B
D
E
B
G
F
0
D
0
0
S(a) = {A}
S(b) = {A,B,C}
S(c) = {A,B,C,D,E}
S(d) = {A,B,C,D,E}
S(e) = {A,B,D,E}
S(f) = {A,D,F}
S(g) = {D,F,G}
S(h) = {D,G,H}
S(i) = {D,G,H}
S(j) = {G,H}
S(k) = {G}
A
B
Lower bound on the number of tracks = 5
a b c d e f g h i j k
Zone representation

## Slide 24: Zone Representation: {A, B, C}
0
B
D
E
B
G
F
0
D
0
0
Column a b c d e f g h i j k
A
C
E
C
E
A
F
H
H
G
0
B
A
C
D
E
F
G
H
A
C
E
C
E
A
F
H
H
G
0
0
B
D
E
B
G
F
0
D
0
0
S(a) = {A}
S(b) = {A,B,C}
S(c) = {A,B,C,D,E}
S(d) = {A,B,C,D,E}
S(e) = {A,B,D,E}
S(f) = {A,D,F}
S(g) = {D,F,G}
S(h) = {D,G,H}
S(i) = {D,G,H}
S(j) = {G,H}
S(k) = {G}
A
B
C
Lower bound on the number of tracks = 5
a b c d e f g h i j k
Zone representation

## Slide 25: Zone Representation: {A, B, C, D}
0
B
D
E
B
G
F
0
D
0
0
Column a b c d e f g h i j k
A
C
E
C
E
A
F
H
H
G
0
B
A
C
D
E
F
G
H
A
C
E
C
E
A
F
H
H
G
0
0
B
D
E
B
G
F
0
D
0
0
S(a) = {A}
S(b) = {A,B,C}
S(c) = {A,B,C,D,E}
S(d) = {A,B,C,D,E}
S(e) = {A,B,D,E}
S(f) = {A,D,F}
S(g) = {D,F,G}
S(h) = {D,G,H}
S(i) = {D,G,H}
S(j) = {G,H}
S(k) = {G}
A
B
C
D
Lower bound on the number of tracks = 5
a b c d e f g h i j k
Zone representation

## Slide 26: Zone Representation: {A, B, C, D, E}
0
B
D
E
B
G
F
0
D
0
0
Column a b c d e f g h i j k
A
C
E
C
E
A
F
H
H
G
0
B
A
C
D
E
F
G
H
A
C
E
C
E
A
F
H
H
G
0
0
B
D
E
B
G
F
0
D
0
0
S(a) = {A}
S(b) = {A,B,C}
S(c) = {A,B,C,D,E}
S(d) = {A,B,C,D,E}
S(e) = {A,B,D,E}
S(f) = {A,D,F}
S(g) = {D,F,G}
S(h) = {D,G,H}
S(i) = {D,G,H}
S(j) = {G,H}
S(k) = {G}
A
B
C
D
E
Lower bound on the number of tracks = 5
a b c d e f g h i j k
Zone representation

## Slide 27: Zone Representation: {A, B, C, D, E, F}
0
B
D
E
B
G
F
0
D
0
0
Column a b c d e f g h i j k
A
C
E
C
E
A
F
H
H
G
0
B
A
C
D
E
F
G
H
A
C
E
C
E
A
F
H
H
G
0
0
B
D
E
B
G
F
0
D
0
0
S(a) = {A}
S(b) = {A,B,C}
S(c) = {A,B,C,D,E}
S(d) = {A,B,C,D,E}
S(e) = {A,B,D,E}
S(f) = {A,D,F}
S(g) = {D,F,G}
S(h) = {D,G,H}
S(i) = {D,G,H}
S(j) = {G,H}
S(k) = {G}
A
B
C
D
F
E
Lower bound on the number of tracks = 5
a b c d e f g h i j k
Zone representation

## Slide 28: Zone Representation: {A, B, C, D, E, F, G}
0
B
D
E
B
G
F
0
D
0
0
Column a b c d e f g h i j k
A
C
E
C
E
A
F
H
H
G
0
B
A
C
D
E
F
G
H
A
C
E
C
E
A
F
H
H
G
0
0
B
D
E
B
G
F
0
D
0
0
S(a) = {A}
S(b) = {A,B,C}
S(c) = {A,B,C,D,E}
S(d) = {A,B,C,D,E}
S(e) = {A,B,D,E}
S(f) = {A,D,F}
S(g) = {D,F,G}
S(h) = {D,G,H}
S(i) = {D,G,H}
S(j) = {G,H}
S(k) = {G}
A
B
C
D
F
G
E
Lower bound on the number of tracks = 5
a b c d e f g h i j k
Zone representation

## Slide 29: Zone Representation: {A, B, C, D, E, F, G, H}
0
B
D
E
B
G
F
0
D
0
0
Column a b c d e f g h i j k
A
C
E
C
E
A
F
H
H
G
0
B
A
C
D
E
F
G
H
A
C
E
C
E
A
F
H
H
G
0
0
B
D
E
B
G
F
0
D
0
0
S(a) = {A}
S(b) = {A,B,C}
S(c) = {A,B,C,D,E}
S(d) = {A,B,C,D,E}
S(e) = {A,B,D,E}
S(f) = {A,D,F}
S(g) = {D,F,G}
S(h) = {D,G,H}
S(i) = {D,G,H}
S(j) = {G,H}
S(k) = {G}
A
B
C
D
F
G
H
E
Lower bound on the number of tracks = 5
a b c d e f g h i j k
Zone representation

## Slide 30: Vertical Constraint Graph
A directed edge e(i,j) connects nodes i and j if the horizontal segment of net i must be located above net j
B
A
A
B

## Slide 31: Vertical Constraint Graph
A
0
B
D
E
B
G
F
0
D
0
0
A
C
E
C
E
A
F
H
H
G
0

## Slide 32: Vertical Constraint Graph
B
C
A
0
B
D
E
B
G
F
0
D
0
0
A
C
E
C
E
A
F
H
H
G
0

## Slide 33: Vertical Constraint Graph
E
D
A
0
B
D
E
B
G
F
0
D
0
0
A
C
E
C
E
A
F
H
H
G
0
B
C

## Slide 34: Vertical Constraint Graph
0
B
D
E
B
G
F
0
D
0
0
A
C
E
C
E
A
F
H
H
G
0
E
D
A
B
C

## Slide 35: Vertical Constraint Graph
Vertical Constraint Graph (VCG)
0
B
D
E
B
G
F
0
D
0
0
A
C
E
C
E
A
F
H
H
G
0
Note: an edge that can be derived by transitivity is not included, such as edge (B,C)
E
D
A
B
C

## Slide 36: Vertical Constraint Graph
0
B
D
E
B
G
F
0
D
0
0
A
C
E
C
E
A
F
H
H
G
0
F
E
D
A
B
C

## Slide 37: Vertical Constraint Graph
0
B
D
E
B
G
F
0
D
0
0
A
C
E
C
E
A
F
H
H
G
0
G
F
E
D
A
B
C

## Slide 38: Vertical Constraint Graph
0
B
D
E
B
G
F
0
D
0
0
A
C
E
C
E
A
F
H
H
G
0
H
G
F
E
D
A
B
C

## Slide 39: Vertical Constraint Graph – Final
B
E
C
D
A
F
G
H
0
B
D
E
B
G
F
0
D
0
0
A
C
E
C
E
A
F
H
H
G
0

## Slide 40: Is Vertical Constrain Graph Acyclic?
A
B
B
B
0
A
A
B
B
A
A
B
B
Cyclic conflict

## Slide 41: Left-Edge Channel Routing Algorithm
Based on the VCG and the zone representation, greedily maximizes the usage of each track
  VCG: assignment order of nets to tracks
  Zone representation: determines which nets may share the same track
Each net uses only one horizontal segment

## Slide 42: Left-Edge Algorithm: Pseudo Code
Input: channel routing instance CR
Output: track assignments for each net
curr_track = 1 // start with topmost track
nets_unassigned = Netlist
while (nets_unassigned != Ø) // while nets still unassigned
VCG = VCG(CR) // generate VCG and zone
ZR = ZONE_REP(CR) // representation
SORT(nets_unassigned,start column) // find left-to-right ordering
// of all unassigned nets
for (i =1 to |nets_unassigned|)
curr_net = nets_unassigned[i]
if (PARENTS(curr_net) == Ø && // if curr_net has no parent
(TRY_ASSIGN(curr_net,curr_track)) // and does not cause // conflicts on curr_track,
ASSIGN(curr_net,curr_track) // assign curr­_net
REMOVE(nets_unassigned,curr_net)
curr_track = curr_track + 1 // consider next track

## Slide 43: Walkthrough – I
0
A
D
E
A
G
F
0
D
I
J
J
B
C
E
C
E
B
F
H
I
H
G
I

## Slide 44: Walkthrough – II
Generate VCG and zone representation
A
E
C
J
D
B
F
G
H
I
A
G
B
H
C
I
D
J
E
F
0
A
D
E
A
G
F
0
D
I
J
J
B
C
E
C
E
B
F
H
I
H
G
I

## Slide 45: Walkthrough – III
A
G
B
H
C
I
D
J
E
F
Consider next track
Find left-to-right ordering of all unassigned nets If curr_net has no parents and does not cause conflicts on curr_track assign curr_net
curr_track = 1:
Net J
Net A
E
C
D
B
F
G
H
I
J
A
  4. Delete placed nets (A, J ) in VCG and zone represenation

## Slide 46: Walkthrough – IV
B
C
E
C
E
B
F
H
I
H
G
I
curr_track = 1
2
3
4
5
0
A
D
E
A
G
F
0
D
I
J
J

## Slide 47: Walkthrough – V
curr_track = 2:
E
C
B
F
G
H
I
G
H
C
I
D
E
F
Net D
  4. Delete placed nets (D ) in VCG and zone representation
B
Consider next track
Find left-to-right ordering of all unassigned nets If curr_net has no parents and does not cause conflicts on curr_track assign curr_net
D

## Slide 48: Walkthrough – VI
B
C
E
C
E
B
F
H
I
H
G
I
1
curr_track = 2
3
4
5
0
A
D
E
A
G
F
0
D
I
J
J

## Slide 49: Walkthrough – VII
curr_track = 3:
E
C
B
F
G
H
I
G
H
C
I
E
F
Net E
Net G
  4. Delete placed nets (E, G ) in VCG and zone representation
B
Consider next track
Find left-to-right ordering of all unassigned nets If curr_net has no parents and does not cause conflicts on curr_track assign curr_net

## Slide 50: Walkthrough – VIII
B
C
E
C
E
B
F
H
I
H
G
I
1
2
curr_track = 3
4
5
0
A
D
E
A
G
F
0
D
I
J
J

## Slide 51: Walkthrough – IX
curr_track = 4:
C
B
F
H
I
H
C
I
F
Net C
Net F
Net I
  4. Delete placed nets (C, F, I ) in VCG and zone representation
B
Consider next track
Find left-to-right ordering of all unassigned nets If curr_net has no parents and does not cause conflicts on curr_track assign curr_net

## Slide 52: Walkthrough – X
B
C
E
C
E
B
F
H
I
H
G
I
1
2
3
curr_track = 4
5
0
A
D
E
A
G
F
0
D
I
J
J

## Slide 53: Walkthrough – XI
curr_track = 5:
B
H
B
H
Net B
Net H
  4. Delete placed nets (B, H ) in VCG and zone representation
Consider next track
Find left-to-right ordering of all unassigned nets If curr_net has no parents and does not cause conflicts on curr_track assign curr_net

## Slide 54: Walkthrough – XII
B
C
E
C
E
B
F
H
I
H
G
I
1
2
3
4
curr_track = 5
Routing result
0
A
D
E
A
G
F
0
D
I
J
J

## Slide 55: Summary
We have discussed channel routing
  Horizontal constraint graph
  Vertical constraint graph
We have discussed left-edge routing algorithm
  Vertical constraint graph & zone representation
  Greedy assignment to maximize the utilization
  Assign a new track whenever needed