## Slide 1
OpenTimer: A high-performance timing analysis tool
Tsung-Wei Huang and Martin D. F. Wong
Department of Electrical and Computer Engineering (ECE)
University of Illinois at Urbana-Champaign (UIUC), IL, USA
https://github.com/OpenTimer/OpenTimer
Notes: ECE Main Slide

## Slide 2
Outline
Problem formulation recap
  Incremental timing and incremental CPPR
OpenTimer architecture
  Tool overview and features
  Core algorithm (IO, graph reduction, pipeline scheduling)
Experimental results
  TAU 2015 contest benchmarks
Conclusion

## Slide 3
Problem Formulation – TAU 2015 Contest
A tool deals with incremental timing and incremental CPPR
  Important for timing-driven applications
  Fast full timing and incremental timing analysis
  Capability of path-based CPPR analysis
  Parallel programming and multi-threading
CPPR impact
(reduction of unwanted pessimism)
*CPPR stands for Common Path Pessimism Removal

## Slide 4
OpenTimer Architecture
An open-source high-performance timing analysis tool
  TAU14 (1st place), TAU15 (2nd place)
  ICCAD15 (golden timer), TAU16 (golden timer)
Feature highlights
  C++11
  Industry format
  STA engine
  Block-based
  Path-based
  Incremental
  Lazy evaluation
  CPPR
  Multi-threaded
https://github.com/OpenTimer/OpenTimer

## Slide 5
Initialize the Timer – Parallel IO
A set of design files that follow the industry standard format
  Verilog netlist, two libraries (early and late), parasitic spef, etc.
  Time-consuming IO (e.g., file IO, complex parsing)
Input files (industry standard)
Verilog (.v)
Liberty (.lib)
Design Parasitics
Assertions
Operations
SPEF (.spef)
(.ops)
(.timing)
Based on TAU 2013, ISPD 2013, ICCAD 2014, Cadence Benchmarks
Early and Late Libraries
Design Connectivity
Task graph
Library (Early)
Verilog
Library (Late)
Build internal data structure
Parasitic
LEF
DEF
Assertion
Parallel dependency generation using portable OpenMP
#pragma parallel …
#pragma task ...
x2 speedup by parallel read/parse!

## Slide 6
Timing Graph Reduction
Reduce the search space
  Identify tree-structured subgraphs in the original timing graph
  Merge every leaf-root path (transition-definite)
R
F
F
R
R
Every leaf-root path can be uniquely defined
(given a transition at an endpoint)
~30% reduction on the graph size
Apply to combinational circuits only

## Slide 7
Key Components of Incremental Timing
Full timing is just a special case of incremental timing
Design modifiers
  Pin-level operations, net-level operations, and gate-level operations
Timing queries
  Slack
  Arrival time
  Required time
  TNS and WNS
  Critical path report
  CPPR
Source of propagation
Lazy evaluation
Explore parallel incremental timing

## Slide 8
Identify the Source of Incremental Timing (I)
Source of incremental timing
  Pins where the next timing propagation must originate from
  Referred to as “frontier pins”
Repower gate (gate sizing)
  repower_gate<gate_name, new_cell_name>
Go one-level up from the gate
Frontier pins
(FF1:Q and FF2:Q)

## Slide 9
Identify the Source of Incremental Timing (II)
Disconnect pin (disconnect a pin from its net)
  disconnect_pin <pin_name>
Affect RC network only
  Incremental timing from the root
Find the root of the corresponding RC network (RC tree)
Frontier pins
(I1:O and FF3:D)
Load cap changed

## Slide 10
Identify the Source of Incremental Timing (III)
Connect pin (connect a pin to a net)
  connect_pin <pin_name, net_name>
Affect RC network only
  Incremental timing from the root
Find the root of the corresponding RC network (RC tree)
Load cap changed
Frontier pins
(I1:O and FF3:D)

## Slide 11
Dealing with Design Modifiers
Design modifiers can be built upon pin-level modification
  remove_net: disconnect all pins and remove the net
  insert_net: create an empty net
  insert_gate: insert a gate and create pins
  remove_gate: disconnect all input and output pins, and remove the gate
  …
How to store frontier pins for correct timing propagation?
  Timing graph is a directed acyclic graph (DAG)
  Efficient data structure, bucketlist, to maintain the dependency
    Apply topological sort (longest path finding)
    Level index of each pin to keep track of dependency
    Every frontier pin is inserted into the corresponding bucket
    Incremental topological sort for incremental levelization

## Slide 12
Pipeline-based Parallel Timing Propagation
Timing propagation has several linearly dependent tasks
  RC update  Slew & Delay  Arrival time  Jump point  CPPR
  Pipeline scheduling with multiple threads
We use the following paper for dealing with CPPR
*UI-Timer: An ultra-fast clock network pessimism removal algorithm, T.-W. Huang, P.-C. Wu, and Martin D. F. Wong, ICCAD14

## Slide 13
Experimental Results – Environment Setup
Implementation
  C++11 with GCC 4.8
  Linux machine (8 cores)*
Benchmark suite
  TAU15 contest benchmarks
Baseline on TAU15 winners
  iTimerC 2.0 (1st place)
  iitRACE (3rd place)
*clock tree has inverters and buffers
*
*
*
*
7 based on released benchmarks (~102 – ~105 gates)
6 based on ICCAD 2014 benchmarks (~105 – ~106 gates)
3 based on Cadence benchmarks (~102 – ~105 gates)
*Campus cluster, University of Illinois at Urbana-Champaign (UIUC)
https://campuscluster.illinois.edu/

## Slide 14
Experimental Results – Overall Performance Comparison
*iTimerC 2.0: 1st place in TAU contest 2015 (binary from authors)
*iitRACE: 3rd place in TAU contest 2015 (binary from authors)

## Slide 15
Experimental Results – Performance Highlights
OpenTimer performance highlights
  Achieved the highest accuracy (both path-based and value-based)
  Achieved the fastest runtime (x2 to x9 speedup)
  Robust and reliable (no crash)
  Small memory usage*
Comparison to the newest results of iTimerC 2.0**
  netcard (1.5M gates and 1.5M nets)
    OpenTimer: 192s, 20GB
    iTimerC 2.0: 213s, 21GB
  leon3mp (1.2M gates and 1.2M nets)
    OpenTimer: 163s, 18GB
    iTimerC 2.0: 186s, 19GB
* Our contest version has higher memory usage is due to the different system environment settings between IBM machine and UIUC machine
**iTimerC 2.0: Fast incremental timing and CPPR analysis, ICCAD15
iTimerC 2.0 runs in 3.5GHz CPU!
OpenTimer runs in 2.2GHz CPU!

## Slide 16
Experimental Results – Scalability of Incremental Timing
Optimization or synthesis tools
  Call an incremental timer millions of times to optimize the timing objective
One incremental processing stage
  A set of design modifiers followed by a timing query
Insufficiency of TAU15 benchmarks
  Only 5~10 incremental processing stages…
x115 speedup by OpenTimer
(at 1459th stage)
X2.7 speedup by OpenTimer
(at 1th stage, i.e. full timing)
Notes: Our tool is truly incremental

## Slide 17
Experimental Results – Parallelism Comparison
Capability of multi-threading
  Higher parallelism translates to higher cpu usage
  Better resource utilization reflects on higher cpu usage
Parallel IO by OpenTimer
Parallel timing by OpenTimer
Single thread by iTimerC 2.0
(no parallelism)

## Slide 18
Conclusion
Developed a high-performance timing analysis tool
  Free software and open-source under GPL v3.0
  Industry format (.v, .spef, .lib, .lef, .def, etc.)
  Fast, accurate, and robust
  Multi-threaded and CPPR by default
Recognition
  1st prize in TAU14 contest (full timing with CPPR)
  2nd prize in TAU15 contest (incremental timing with CPPR)
  Golden timer in ICCAD15 CAD contest
  Golden timer in TAU16 contest
Acknowledgment
  Jin, Billy, M.-C., team iTimerC, team iitRACE, and the UIUC CAD group!

## Slide 19
OpenTimer Community