## Slide 1: Lecture 3: Circuit Partitioning – I
Tsung-Wei (TW) Huang
Department of Electrical and Computer Engineering
University of Utah, Salt Lake City, UT

## Slide 2: Physical Design Flow

## Slide 3: Circuit Partition
An essential step for reducing algorithm design complexity
  Divide and conquer (D&C)
Input
  A circuit graph
Output
  A set of partitioned subgraphs
Objective
  Minimize cross-connection

## Slide 4: Importance of Circuit Partition
Divide & Conquer design methodology
  The most effective way to solve problems of high complexity
  Ex: min-cut based placement, partitioning-based test generation, …
System-level partitioning for multi-chip designs
  Inter-chip interconnection delay dominates system performance
Circuit emulation/parallel simulation
  Partition large circuit into multiple FPGAs or multiple special-purpose processors
Parallel CAD development
  Task decomposition and load balancing
In deep-submicron designs, partitioning defines local and global interconnect, and has significant impact on circuit performance

## Slide 5: Application: D&C-based Placement
Notes: Let's take a look at one step of computer design, placement. A placement is a step that tries to find the location of each gate, you know Or gate, NAND gate, NOT gate, and other gates, in a chip area. And we have billions of gate to place in a finger size chip.
Computer design tools don't do this. They do this in divide and conquer. (explain)

## Slide 6: Application: D&C-based Placement

## Slide 7: Application: D&C-based Placement

## Slide 8: Application: D&C-based Placement

## Slide 9: Application: D&C-based Placement

## Slide 10: Application: D&C-based Placement

## Slide 11: Application: D&C-based Placement

## Slide 12: Application: D&C-based Placement
Notes: So, from iteration to iteration you can clearly see cells are placed very regularly, right, Cells are spreading along the 2D grid partition. We partition the large chip care into smaller grids and place cells in those small grids. Solving the smaller grid problem is definitely more efficiently than directly handling the original problem.

## Slide 13: Terminology
Partitioning
  Dividing bigger circuits into a small number of partitions (top down)
Clustering
  Cluster small cells into bigger clusters (bottom up)
Covering / Technology Mapping
  Clustering such that each partition (cluster) has special structure
k-way Partitioning
  Dividing into k partitions
Bipartitioning
  2-way partitioning

## Slide 14: Circuit Representation
Netlist
  Gates: A, B, C, D
  Nets: {A,B,C}, {B,D}, {C,D}
Hypergraph
  Vertices: A, B, C, D
  Hyperedges: {A,B,C}, {B,D}, {C,D}
  Vertex label: Gate size/area
  Hyperedge label:
Importance of net (weight)
A
B
C
D
A
B
C
D

## Slide 15: Circuit Partition Formulation
Minimize interconnections between partitions
Minimum cut: min c(x, x’)
Minimum bisection: min c(x, x’) with |x|= |x’|
Minimum ratio-cut: min c(x, x’) / |x||x’|
X
X’
c(X,X’)

## Slide 16: A Bi-partitioning Example
Min-cut:
Min-bisection cut:
Min-ratio-cut:
a
b
c
e
d
f
mini-ratio-cut
min-bisection
min-cut
9
10
100
100
100
100
100
100
4
Ratio-cut helps to identify natural clusters!
cut size = 13
cut size = 300
cut size = 19

## Slide 17: Circuit Partition Formulation
General multi-way partitioning formulation
  Partition a network N into N1, N2, …, Nk such that
    Each partition has an area constraint
    Each partition has an I/O constraint
  Minimize the total interconnection:
å
Î
£
i
N
v
i
A
v
a
)
(
i
i
i
I
N
N
N
c
£
-
)
,
(
)
,
(
i
N
i
N
N
N
c
i
-
å
3-way partitions (k=3)

## Slide 18: Circuit Partitioning Algorithms
Iterative partitioning algorithms
Spectral based partitioning algorithms
Deterministic vs. probabilistic algorithms
Net partitioning vs. module partitioning
Multi-way partitioning
Multi-level partitioning
Further study in partitioning techniques (timing-driven …)

## Slide 19: Iterative Partitioning Algorithms
Greedy iterative improvement method
  [Kernighan-Lin 1970]
  [Fiduccia-Mattheyses 1982]
  [Krishnamurthy 1984]
  …
Simulated Annealing
  [Kirkpartrick-Gelatt-Vecchi 1983]
  [Greene-Supowit 1984]
  …

## Slide 20: Kernighan-Lin (KL) Algorithm
“An Efficient Heuristic Procedure for Partitioning Graphs,” The Bell System Technical Journal, 49(2):291-307, 1970

## Slide 21: Restricted Partition Problem
Restrictions
  For Bisectioning of circuit (k=2, two-way partitioning)
  Assume all gates are of the same size
  Works only for 2-terminal nets
If all nets are 2-terminal, the hypergraph is called a graph
A
B
C
D
Hypergraph
Representation
Graph
Representation
A
B
C
D

## Slide 22: Problem Formulation
Input: A graph with
  Set vertices V (|V| = 2n)
  Set of edges E (|E| = m)
  Cost cAB for each edge {A, B} in E
Output: 2 partitions X & Y such that
  Total cost of edges cut is minimized
  Each partition has n vertices
This problem has been proven to be NP-complete
  Very difficult to find the optimal partition efficiently

## Slide 23: A Naive Approach …
Try all possible bisections, find the best one
If there are 2n vertices,
# of possibilities =
For 4 vertices (A,B,C,D), 3 possibilities
  1. X={A,B} & Y={C,D}
  2. X={A,C} & Y={B,D}
  3. X={A,D} & Y={B,C}
For 100 vertices, 5x1028 possibilities
  Need 1.59x1013 years if one can try 100M possibilities per second
= (2n)! / (2 × (n!2)) = nO(n)

## Slide 24: Idea of KL Algorithm
DA = Decrease in cut value if moving A
  External cost (connection) EA – Internal cost IA
  Moving node a from block X to block Y would increase the value of the cutset by EA and decrease it by IA
DA =
DB =
= 2-1 = 1
= 1-1 = 0
A
B
C
D
X
Y
A
B
C
D
X
Y

## Slide 25: Idea of KL Algorithm
Note that we want to balance two partitions
If switch A & B, gain(A,B) = Da + Db?
A
B
C
D
X
Y
gain(A,B) = 1+0 = 1?
A
B
C
D
X
Y

## Slide 26: Idea of KL Algorithm
Note that we want to balance two partitions
If switch A & B, gain(A,B) = DA + DB – 2CAB
  cAB : edge cost for AB
A
B
C
D
X
Y
gain(A,B) = 1+0-2 = -1
A
B
C
D
X
Y

## Slide 27: KL Algorithm
Start with any initial legal partitions X and Y
A pass (exchanging each vertex exactly once) is described below:
  1. For i := 1 to n do
  From the unlocked (unexchanged) vertices,
  choose a pair (A,B) s.t. gain(A,B) is largest (greedy)
  Exchange and Lock A, B
  Let gi = gain(A,B)
  2. Find the k s.t. G=g1+...+gk is maximized
  3. Switch the first k pairs
Repeat the pass until there is no improvement (G=0)

## Slide 28: KL Algorithm Walkthrough – 1
1
2
3
4
5
6

## Slide 29: KL Algorithm Walkthrough – 2
1
2
3
4
5
6
D1 =
D2 =
D3 =
D4 =
D5 =
D6 =
gain(2, 1) =
gain(2, 5) =
gain(2, 6) =
gain(3, 1) =
gain(3, 5) =
gain(3, 6) =
gain(4, 1) =
gain(4, 5) =
gain(4, 6) =
1-0 = 1
1-2 = -1
0-1 = -1
2-1 = 1
1-1 = 0
1-1 = 0
-1 + 1 – 2 = -2
-1 + 0 – 0 = -1
-1 + 0 – 0 = -1
-1 + 1 – 0 = 0
-1 + 0 – 0 = -1
-1 + 0 – 0 = -1
1 + 1 – 0 = 2
1 + 0 – 2 = -1
1 + 0 – 2 = -1
4
1
g1

## Slide 30: KL Algorithm Walkthrough – 3
1
2
3
4
5
6
D2 =
D3 =
D5 =
D6 =
gain(2, 5) =
gain(2, 6) =
gain(3, 5) =
gain(3, 6) =
1 – 2 = -1
0 – 1 = -1
0 – 2 = -2
0 – 2 = -2
-1 + -2 – 0 = -3
-1 + -2 – 0 = -3
-1 + -2 – 0 = -3
-1 + -2 – 0 = -3
2
5
g2

## Slide 31: KL Algorithm Walkthrough – 4
1
2
3
4
5
6
D3 =
D6 =
gain(3, 6) =
1 – 0 = 1
1 – 1 = 0
1 – 0 – 0 = 1
1
2
6
4
5
3
3
6
g3
g1 = 2, g2 = -3, g3 = 1
Then ???
We need to find k
k = 1: g1 =
k = 2: g1 + g2 =
k = 3: g1 + g2 + g3 =
2
-1
0

## Slide 32: KL Algorithm Walkthrough – 5
Since k = 1, we only take 1 move  swap (4, 1)
Finally, we get the result? NO! We only go 1 iteration!
Move on to the next iteration until converged
1
2
3
4
5
6
1
2
3
4
5
6

## Slide 33: Recap: KL Algorithm
Start with any initial legal partitions X and Y
A pass (exchanging each vertex exactly once) is as follows:
  1. For i := 1 to n do
  From the unlocked (unexchanged) vertices,
  choose a pair (A,B) s.t. gain(A,B) is largest (greedy)
  Exchange and Lock A, B
  Let gi = gain(A,B)
  2. Find the k s.t. G=g1+...+gk is maximized
  3. Switch the first k pairs
Repeat the pass until there is no improvement (G=0)
A pass

## Slide 34: Time Complexity of KL Algorithm
For each pass of KL
  O(n2) time to find the best pair to exchange
  n pairs exchanged
  Total time is O(n3) per pass
Better implementation can get O(n2log n) time per pass
  But requires fairly sophisticated data structure representation
Number of passes is usually small
  Converged very fast in practice

## Slide 35: Drawbacks of KL Algorithm
Handle only unit vertex weights
  Vertex weights might represent block sizes, different from blocks to blocks in real situation
Handle only exact bisection
  Need dummy vertices to handle the unbalanced problem
Handle only non-hypergraphs
  Practical circuits have many terminal nodes for each cell output
  Need to handle multi-terminal nets directly
A
B
C
D
A has two terminals, B and C!

## Slide 36: Summary of KL Algorithm
1. Pair-wise exchange of nodes to reduce cut size
2. Allow cut size to increase temporarily within a pass
3. Compute the gain of a swap
Repeat
Perform a feasible swap of max gain
Mark swapped nodes “locked”
Update swap gains
Until no feasible swap
4. Find max prefix partial sum in gain sequence g1, g2, …, gm
5. Make corresponding swaps permanent
6. Start another pass if current pass reduces the cut size
u 
v 
v 
u 
locked