## Slide 1: Lecture 4: Circuit Partitioning – II
Tsung-Wei (TW) Huang
Department of Electrical and Computer Engineering
University of Utah, Salt Lake City, UT

## Slide 2: Recap: Circuit Partition
An essential step for reducing algorithm design complexity
  Divide and conquer (D&C)
Input
  A circuit graph
Output
  A set of partitioned subgraphs
Objective
  Minimize cross-connection

## Slide 3: Recap: KL Algorithm
1. Pair-wise exchange of nodes to reduce cut size
2. Allow cut size to increase temporarily within a pass
3. Compute the gain of a swap
Repeat
Perform a feasible swap of max gain
Mark swapped nodes “locked”
Update swap gains
Until no feasible swap
4. Find max prefix partial sum in gain sequence g1, g2, …, gm
5. Make corresponding swaps permanent
6. Start another pass if current pass reduces the cut size
u 
v 
v 
u 
locked

## Slide 4: Recap: Drawbacks of KL Algorithm
Handle only unit vertex weights
  Vertex weights might represent block sizes, different from blocks to blocks in real situation
Handle only exact bisection
  Need dummy vertices to handle the unbalanced problem
Handle only non-hypergraphs
  Practical circuits have many terminal nodes for each cell output
  Need to handle multi-terminal nets directly
A
B
C
D
A has two terminals, B and C!

## Slide 5: Fiduccia-Mattheyses (FM) Algorithm
Fiduccia and Mattheyses, “A linear time heuristic for improving network partitions,” ACM Design Automation Conference (DAC), 1982
Cell gains based on “net”

## Slide 6: Hypergraph Partition Problem Formulation
Input: A hypergraph with
  Set vertices V. (|V| = n)
  Set of hyperedges E (total # pins in netlist = p)
  Area au for each vertex u in V
  Cost ce for each hyperedge in e
  An area ratio r
Output: two partitions X & Y such that
  Total cost of hyperedges cut is minimized
  area(X) / (area(X) + area(Y)) is about r
This problem has been proven to be NP-complete

## Slide 7: Ideas of FM Algorithm
Similar to KL:
  Work in passes
  Lock vertices after moved
  Only move those vertices up to the maximum partial sum of gain
Difference from KL:
  Not exchanging pairs of vertices
    Move only one vertex at each time
  Calculate the gain value based on connected nets
  The use of gain bucket data structure

## Slide 8: FM Partitioning Algorithm
Moves are made based on object gain
Object Gain: The amount of change in cut crossings that will occur if an object is moved from its current partition into the other partition
A pass description
While there is unlocked object
1. Each object is assigned a gain
2. Objects are put into a sorted gain list
3. The object with the highest gain from the larger of the two sides is selected and moved
4. The moved object is "locked"
5. Gains of "touched" objects are recomputed
6. Gain lists are resorted
Repeat the pass until there is no improvement

## Slide 9: FM Algorithm Walkthrough – 1
-1
-2
-1
1
0
0
2
0
0
1
-1
-1
-2
0
Let’s focus on 2-pin net first for simplicity
(degenerate to KL)

## Slide 10: FM Algorithm Walkthrough – 2
-1
-2
-1
1
0
0
0
2
0
0
1
-1
-1
-2

## Slide 11: FM Algorithm Walkthrough – 3
-1
-2
-1
1
-2
-2
0
1
-1
-1
-2
-2
0
0

## Slide 12: FM Algorithm Walkthrough – 4
-1
-2
-1
1
0
-2
-2
0
0
1
-1
-1
-2
-2

## Slide 13: FM Algorithm Walkthrough – 5
-1
-2
-1
1
0
-2
-2
0
0
1
-1
-1
-2
-2

## Slide 14: FM Algorithm Walkthrough – 6
-1
-2
1
-1
0
-2
-2
0
-2
-1
-1
-1
-2
-2

## Slide 15: FM Algorithm Walkthrough – 7
-1
-2
1
-1
0
-2
-2
0
-2
-1
-1
-1
-2
-2

## Slide 16: FM Algorithm Walkthrough – 8
-1
-2
1
-1
0
-2
-2
0
-2
-1
-1
-2
-2
-1

## Slide 17: FM Algorithm Walkthrough – 9
-1
-2
1
-1
-2
-2
-2
0
-2
-1
1
-1
-2
-2

## Slide 18: FM Algorithm Walkthrough – 10
-1
-2
1
-1
-2
-2
-2
0
-2
-1
1
-1
-2
-2

## Slide 19: FM Algorithm Walkthrough – 11
-1
-2
1
-1
-2
-2
-2
0
-2
-1
1
-1
-2
-2

## Slide 20: FM Algorithm Walkthrough – 12
-1
-2
-1
-3
-2
-2
-2
0
-2
-1
1
-1
-2
-2

## Slide 21: FM Algorithm Walkthrough – 13
-1
-2
-3
-2
-2
-2
0
-2
-1
1
-1
-2
-2
-1

## Slide 22: FM Algorithm Walkthrough – 14
-1
-2
-3
-2
-2
-2
0
-2
-1
1
-1
-2
-2
-1

## Slide 23: FM Algorithm Walkthrough – 15
-1
-2
-3
-2
-2
-2
-2
-2
-1
-1
-1
-2
-2
-1

## Slide 24: Implementation Details
Gain g(c) for cell c
g(c) = FS(c) – TE(c) ,
where the “moving force“ FS(c) is the number of nets connected to c but not connected to any other cells within c’s partition, i.e., cut nets that connect only to c, and
the “retention force“ TE(c) is the number of uncut nets connected to c.
The higher the gain g(c), the higher is the priority to move the cell c to the other partition.
1
3
4
2
5
a
b
c
d
e
Netlist: a {1, 2}, b {1, 2, 3}, c {1, 4}, d {1, 5}, e {3, 4}

## Slide 25: Implementation Details (cont’d)
Gain g(c) for cell c
g(c) = FS(c) – TE(c) ,
where the “moving force“ FS(c) is the number of nets connected to c but not connected to any other cells within c’s partition, i.e., cut nets that connect only to c, and
the “retention force“ TE(c) is the number of uncut nets connected to c.
Cell 1: FS(1) = 2 TE(1) = 1 g(1) = 1
Cell 2: FS(2) = 0 TE(2) = 1 g(2) = -1
Cell 3: FS(3) = 1 TE(3) = 1 g(3) = 0
Cell 4: FS(4) = 1 TE(4) = 1 g(4) = 0
Cell 5: FS(5) = 1 TE(5) = 0 g(5) = 1
1
3
4
2
5
a
b
c
d
e
1
3
4
2
5
a
b
c
d
e
Netlist: a {1, 2}, b {1, 2, 3}, c {1, 4}, d {1, 5}, e {3, 4}

## Slide 26: Maximum Positive Gain
Find the maximum positive gain Gm for each pass
The maximum positive gain Gm is the cumulative cell gain of m moves that produce a minimum cut cost.
Gm is determined by the maximum sum of cell gains g over a prefix of m moves in a pass

## Slide 27: Area Ratio Factor
The ratio factor is the relative balance between the two partitions with respect to cell area It is used to prevent all cells from clustering into one partition.
The ratio factor r is defined as
  where area(A) and area(B) are the total respective areas of partition A and partition B

## Slide 28: Balanced Partition
The balance criterion enforces the ratio factor
To ensure feasibility, the maximum cell area areamax(V) must be taken into account
A partitioning of V into two partitions A and B is said to be balanced if
[ r ∙ area(V) – areamax(V) ] ≤ area(A) ≤ [ r ∙ area(V) + areamax(V) ]

## Slide 29: Base Cell
A base cell is a cell c that has the greatest cell gain g(c) among all free cells, and whose move does not violate the balance criterion
Cell 1: FS(1) = 2 TE(1) = 1 g(1) = 1
Cell 2: FS(2) = 0 TE(2) = 1 g(2) = -1
Cell 3: FS(3) = 1 TE(3) = 1 g(3) = 0
Cell 4: FS(4) = 1 TE(4) = 1 g(4) = 0
Base cell

## Slide 30: FM Algorithm (One Pass)
1
3
4
2
5
A
B
a
b
c
d
e
Step 0: Compute the balance criterion
[ r ∙ area(V) – areamax(V) ] ≤ area(A) ≤ [ r ∙ area(V) + areamax(V) ]
0.375 * 16 – 5 = 1  area(A)  11 = 0.375 * 16 +5.
Given: Ratio factor r = 0.375
area(Cell_1) = 2 area(Cell_2) = 4 area(Cell_3) = 1 area(Cell_4) = 4 area(Cell_5) = 5

## Slide 31: FM Algorithm (One Pass)
1
3
4
2
5
A
B
a
b
c
d
e
Step 1: Compute the gains of each cell Cell 1: FS(Cell_1) = 2 TE(Cell_1) = 1 g(Cell_1) = 1
Cell 2: FS(Cell_2) = 0 TE(Cell_2) = 1 g(Cell_2) = -1
Cell 3: FS(Cell_3) = 1 TE(Cell_3) = 1 g(Cell_3) = 0
Cell 4: FS(Cell_4) = 1 TE(Cell_4) = 1 g(Cell_4) = 0
Cell 5: FS(Cell_5) = 1 TE(Cell_5) = 0 g(Cell_5) = 1
FS(c): # cut nets that connect only to c TE(c): # uncut nets connected to c

## Slide 32: FM Algorithm (One Pass)
1
3
4
2
5
A
B
a
b
c
d
e
Step 2: Select the base cell
Possible base cells are Cell 1 and Cell 5
Balance criterion after moving Cell 1: area(A) = area(Cell_2) = 4
Balance criterion after moving Cell 5: area(A) = area(Cell_1) + area(Cell_2) + area(Cell_5) = 11
Both moves respect the balance criterion. Let’s select Cell 1 (can also do Cell 5).
Cell 1: FS(Cell_1) = 2 TE(Cell_1) = 1 g(Cell_1) = 1
Cell 2: FS(Cell_2) = 0 TE(Cell_2) = 1 g(Cell_2) = -1
Cell 3: FS(Cell_3) = 1 TE(Cell_3) = 1 g(Cell_3) = 0
Cell 4: FS(Cell_4) = 1 TE(Cell_4) = 1 g(Cell_4) = 0
Cell 5: FS(Cell_5) = 1 TE(Cell_5) = 0 g(Cell_5) = 1
Ratio factor r = 0.375
area(Cell_1) = 2 area(Cell_2) = 4 area(Cell_3) = 1 area(Cell_4) = 4 area(Cell_5) = 5

## Slide 33: FM Algorithm (One Pass)
1
3
4
2
5
A
B
a
b
c
d
e
Step 3: Fix base cell, update g values
Cell 2: FS(Cell_2) = 2 TE(Cell_2) = 0 g(Cell_2) = 2
Cell 3: FS(Cell_3) = 0 TE(Cell_3) = 1 g(Cell_3) = -1
Cell 4: FS(Cell_4) = 0 TE(Cell_4) = 2 g(Cell_4) = -2
Cell 5: FS(Cell_5) = 0 TE(Cell_5) = 1 g(Cell_5) = -1
After Iteration i = 1: Partition A1 = {2}, Partition B1 = {1,3,4,5}, with fixed cell {1}.
FS(c): # cut nets that connect only to c TE(c): # uncut nets connected to c

## Slide 34: FM Algorithm (One Pass)
1
3
4
2
5
A
B
a
b
c
d
e
Next iteration …
Cell 2 has maximum gain g2 = 2, area(A) = 0, balance criterion is violated
Cell 3 has next maximum gain g2 = -1, area(A) = 5, balance criterion is met
Cell 5 has next maximum gain g2= -1, area(A) = 9, balance criterion is met
Move cell 3, updated partitions: A2 = {2,3}, B2 = {1,4,5}, with fixed cells {1,3}
Cell 2: FS(Cell_2) = 2 TE(Cell_2) = 0 g(Cell_2) = 2
Cell 3: FS(Cell_3) = 0 TE(Cell_3) = 1 g(Cell_3) = -1
Cell 4: FS(Cell_4) = 0 TE(Cell_4) = 2 g(Cell_4) = -2
Cell 5: FS(Cell_5) = 0 TE(Cell_5) = 1 g(Cell_5) = -1
Lock Cell 1

## Slide 35: FM Algorithm (One Pass)
1
3
4
2
5
A
B
a
b
c
d
e
Next iteration …
Cell 2 has maximum gain g3 = 1, area(A) = 1, balance criterion is met. Move cell 2, updated partitions: A3 = {3}, B3 = {1,2,4,5}, with fixed cells {1,2,3}
Cell 2: g(Cell_2) = 1
Cell 4: g(Cell_4) = 0
Cell 5: g(Cell_5) = -1
Lock Cell 1 and Cell 3

## Slide 36: FM Algorithm (One Pass)
1
3
4
2
5
B
A
a
b
c
d
e
Next iteration …
Cell 4 has maximum gain g4 = 0, area(A) = 5, balance criterion is met. Move cell 4, updated partitions: A4 = {3,4}, B3 = {1,2,5}, with fixed cells {1,2,3,4}
Cell 4: g(Cell_4) = 0
Cell 5: g(Cell_5) = -1
Lock Cell 1, Cell 3, and Cell 2

## Slide 37: FM Algorithm (One Pass)
1
3
4
2
5
B
A
a
b
c
d
e
Next iteration …
Cell 5 has maximum gain g5 = -1, area(A) = 10, balance criterion is met. Move cell 5, updated partitions: A4 = {3,4,5}, B3 = {1,2}, all cells {1,2,3,4,5} fixed.
Cell 5: g(Cell_5) = -1
Lock Cell 1, Cell 3, Cell 2, and Cell 4

## Slide 38: FM Algorithm (One Pass)
1
3
4
2
5
B
A
a
b
c
d
e
found in iterations 1, 3 and 4.
The move prefix m = 4 is selected due to the better balance ratio (area(A) = 5); the four cells 1, 2, 3 and 4 are then moved.
Result of Pass 1: Current partitions: A = {3,4}, B = {1,2,5}, cut cost reduced from 3 to 2.
Maximum positive cumulative gain
End of each pass: find best move sequence c1 … cm
G1 = g1 = 1 G2 = g1 + g2 = 0 G3 = g1 + g2 + g3 = 1 G4 = g1 + g2 + g3 + g4 = 1 G5 = g1 + g2 + g3 + g4 + g5 = 0.
Ratio factor r = 0.375
area(Cell_1) = 2 area(Cell_2) = 4 area(Cell_3) = 1 area(Cell_4) = 4 area(Cell_5) = 5

## Slide 39: Gain-based Bucket Data Structure
Cell
#
Cell
#
Max
Gain
+pmax
-pmax
1
2
n

## Slide 40: Incremental Update
Which gain values need update after moving Cell 3?
1
3
4
2
5
A
B
a
b
c
d
e
1
3
4
2
5
A
B
a
b
c
d
e

## Slide 41: Time Complexity of FM Algorithm
For each pass
  Constant time to find the best vertex to move
  After each move, time to update gain buckets is proportional to degree of vertex moved
  Total time is O(p), where p is total number of pins
Number of passes is usually small
  Gain values converge very quickly

## Slide 42: Programming Assignment #1
Implement FM partitioning algorithm
  https://github.com/tsung-wei-huang/ece5960-physical-design/tree/main/PA1
Two checkpoint dues, 9/7 and 9/14 23:59 PM
  https://github.com/tsung-wei-huang/ece5960-physical-design/issues/2
Final Due on 9/21 (Wed) 23:59 PM
  Upload your solutions to twhuang-server-01.ece.utah.edu
    Account: ece6960-fall22
  Place your source code + README under PA1/your_uid/
  README should contain instruction to compile & run your code

## Slide 43: Programming Assignment #1 (cont’d)
In addition to source code + README, upload a report with:
  A table showing your results of each benchmark
  A section discussing what challenges you encounter
  A section discussing how you overcome those challenges
    Also discuss unsolved challenges
The report needs to be just a one- or two-page pdf
  No need to be lengthy …
Upload your report to the class GitHub page
  https://github.com/tsung-wei-huang/ece5960-physical-design/issues/1
  Due 9/21 23:59 PM

## Slide 44: In-class Presentation: 9/14
Circuit partition research presentation on 9/14 (in class)
  George Karypis and Vipin Kumar, "Multilevel k-way Hypergraph Partitioning," 1999 ACM/IEEE Design Automation Conference (DAC)
  Honghua Yang and Martin Wong, "Efficient Network Flow Based Min-Cut Balanced Partitioning," 1994 ACM/IEEE International Conference on Computer-aided Design (ICCAD)
  Masahiro Tanaka, Kenjiro Taura, Toshihiro Hanawa, Kentaro Torisawa, "Automatic Graph Partitioning for Very Large-scale Deep Learning," 2021 IEEE International Parallel and Distributed Processing Symposium (IPDPS 2021)
https://github.com/tsung-wei-huang/ece5960-physical-design/issues/9

## Slide 45: Summary
We have discussed FM partitioning algorithm
  Inherited greedy movement ideas from KL algorithm
  Extended to hypergraph
  Incorporated area constraint (balanced partition)
We have discussed implementation details of FM algorithm
  Bucket list data structure to keep track of gains and cells
  Incremental update for gain values