## Slide 1: Lecture 7: Floorplan – I
Tsung-Wei (TW) Huang
Department of Electrical and Computer Engineering
University of Utah, Salt Lake City, UT

## Slide 2: Physical Design Flow

## Slide 3: Floorplanning
Module e
Module d
Module c
Module b
Module a
Floorplanning
GND
VDD
I/O Pads
Block Pins
Block a
Block b
Block d
Block e
Floorplan
Block c
Supply Network
Partitioned modules (e.g., FM algorithm)

## Slide 4: Floorplanning Problem
The floorplanning problem is to plan the positions and shapes of the modules at the beginning of the design cycle to optimize the circuit performance…
  chip area
  total wirelength
  delay of critical path
  routability
  others, ex: noise, heat dissipation, …

## Slide 5: Floorplanning Example
Given three blocks with the following potential widths & heights
  Block A: w = 1, h = 4 or w = 4, h = 1 or w = 2, h = 2
  Block B: w = 1, h = 2 or w = 2, h = 1
  Block C: w = 1, h = 3 or w = 3, h = 1
Goal: Pack a floorplan with minimum total area enclosed
A
A
A
B
B
C
C
Floorplanning
A
C
B

## Slide 6: Floorplanning Problem Formulation
Input:
  n Blocks with areas A1, ... , An
  Bounds ri and si on the aspect ratio of block Bi
Output:
  Coordinates (xi, yi), width wi and height hi for each block such that hi wi = Ai and ri  hi/wi  si
Objective:
  To optimize the circuit performance

## Slide 7: Bounds on Aspect Ratio
If there is no bound on the aspect ratios, can we pack everything tightly?
But we don’t want to layout blocks as long strips, so we require ri  hi/wi  si for each i
Floorplanning

## Slide 8: Bounds on Aspect Ratio (cont’d)
In practice, we allow several shapes for soft blocks
For hard blocks, the orientations can be changed
  E.g., rotate by 90 degree

## Slide 9: Wirelength Estimation
Exact wirelength of each net is unknown until routing
  Gate-to-gate connection is routed/established via “wire”
Some possible wirelength estimations:
  Center-to-center estimation
  Half-perimeter wirelength (HPWL) estimation
Center-to-center
Half-perimeter wirelength

## Slide 10: Dead Space
Dead space is the space that is wasted
Minimizing area is the same as minimizing dead space
Dead space percentage is computed as
(A - iAi) / A  100%
Dead space (while space)

## Slide 11: Objective Function
A commonly used objective function is a weighted sum of area (or dead space area) and wirelength
cost = aA + bL
  A is the total area of the packing
  L is the total wirelength
  a and b are tuning parameters

## Slide 12: Slicing Floorplan
Slicing floorplan
  One that can be obtained by repetitively subdividing (slicing) rectangles horizontally or vertically
Non-slicing floorplan
  One that may not be obtained by repetitively subdividing alone
Slicing floorplans are much easier to handle
  Efficient data structures exist for efficient computational manipulations
Slicing Floorplan
Non-slicing Floorplan

## Slide 13: Representation of Slicing Floorplan
6
2
3
5
4
7
1
Slicing Floorplan
V
H
H
2
1
3
H
V
6
4
V
7
5
Slicing Tree
21H67V45VH3HV
Polish Expression: Postorder traversal of the slicing tree
Q: Is slicing tree unique?

## Slide 14: Slicing Tree is NOT Unique
b
d
a
e
c
f
a
c
b
d
e
f
H
V
H
H
V
H
V
H
d
c
e
f
H
V
b
a
Alternatively …
Two possible slicing trees representing the same floorplan

## Slide 15: Polish Expression
Succinct representation of slicing floorplan
  Roughly specifying relative positions of blocks
Postorder traversal of slicing tree algorithm (recursive)
  1. Call postorder traversal of left sub-tree
  2. Call postorder traversal of right sub-tree
  3. Print the label of the current root
For n blocks, a Polish Expression contains n operands (blocks) and n-1 operators (H, V)
However, for a given slicing floorplan, the corresponding slicing tree (and hence polish expression) is not unique. Therefore, there is some redundancy in the representation

## Slide 16: Redundancy of Polish Expression
Recall that the slicing tree representation is not unique
6
2
3
5
4
7
1
V
H
H
2
1
3
H
V
6
4
V
7
5
21H67V45VH3HV
V
H
H
2
1
H
V
6
V
7
3
4
5
21H67V45V3HHV

## Slide 17: Skewed and Normalized Slicing Tree
Skewed Slicing Tree: no node and its right son are the same
Normalized Polish Expression: no consecutive H’s or V’s
6
2
3
5
4
7
1
V
H
H
2
1
3
H
V
6
4
V
7
5
21H67V45VH3HV
V
H
H
2
1
H
V
6
V
7
3
4
5
21H67V45V3HHV
Skewed slicing tree
(also normalized)
Not normalized!

## Slide 18: Normalized Polish Expression
There is a 1-1 correspondence between Slicing Floorplan, Skewed Slicing Tree, and Normalized Polish Expression
Can we use Normalized Polish Expression (NPE) to represent slicing floorplans?
  What is a valid NPE?
We formulate as a state space search problem

## Slide 19: Solution Representation
An expression E = e1e2…e2n-1, where ei  {1, 2, …, n, H, V}, 1i 2n-1, is a valid Polish expression of length 2n-1 if
  every operand j, 1  j n, appears exactly once in E;
  for every sub-expression Ei = e1…ei, 1 i 2n-1, #operands > #operators.
Polish expression  Postorder traversal.
ijH: i below j; ijV: i on the left of j.

## Slide 20: Example
12VH3: invalid
123VH: valid
1234567HHHHVV: valid
1HVVHHV743526: invalid

## Slide 21: How to Remove Redundant Rep?

## Slide 22: Neighborhood Structure
Chain: HVHVH… or VHVHV…
The moves:
  M1: Swap adjacent operands (ignoring chains)
  M2: Complement some chain
  M3: Swap 2 adjacent operand and operator
    M3 can give you some invalid NPE. Checking for validity after M3 is needed
It can be proved that every pair of valid NPE are connected
16H35V2HV74HV
Chains

## Slide 23: Example of Moves
2
1
5
4
3
1
4
3
2
5
32V4H5V1H
1
5
4
2
3
32V45HV1H
1
4
5
3
2
32V45VH1H
M1
M3
M2
34V2H5V1H
Each move gives a new floorplan result
Key idea: try out many moves and acquire the best solution?

## Slide 24: Example of Moves (cont’d)
12V4H3V
12H3H4V
12H34HV
M1
M2
M3
12V3H4V
Optimal result is acquired after three moves, M1, M2, and M3
Initial State
New solution 1
New solution 2
New solution 2
…
M1
M2
M3
Can we solve this systematically?

## Slide 25: Simulated Annealing (SA) Algorithm
1 begin
2 Get an initial solution S;
3 Get an initial temperature T > 0;
4 while not yet “frozen” do
5 for 1 i P do
6 Pick a random neighbor S’ of S;
7 △ cost(S’) – cost(S); /* down hill move */
8 if △ 0 then SS’ /* uphill move */
9 if △ > 0 then SS’ with probability;
10 TrT ; /* reduce temperature */
11 return S
12 end
State S
cost (S)

## Slide 26: SA-based Floorplan Optimization
Ti = aTi-1 where a=0.85
At each temperature, try k × n moves
  k is around 5 to 10
Terminate the annealing process if
  either # of accepted moves < 5%
  or the temperature is low enough
Cost metric: aA + bL
  Area + Wirelength
2
3
1
....
n
Initial State: 1V2V3V…nV

## Slide 27: Result of SA-based Floorplan

## Slide 28: How Do We Know the Area from a PE?
Binary operator: V and H
  V: maximum on width and summation on height
  H: maximum on height and summation on width
1
2
H
1
2
3
4
V
3
4
(a) Postfix expression: 12H
(b) Postfix expression: 34V
H12
W12
W12= max(W1 , W2)
H12= H1 + H2
W34 = W3 + W4
H34 = max(H3 , H4)
H34
W34

## Slide 29: Recover Area Recursively
Binary operator: V and H
  V: maximum on width and summation on height
  H: maximum on height and summation on width
1
2
H
1
2
3
4
V
3
4
V
H1234
W1234
W1234 = W12 + W34
H1234 = max(H12 , H34)
(c) Postfix expression: 12H34VV
Bottom-up merging left and right subtrees

## Slide 30: Recover Area Recursively (cont’d)
Binary operator: V and H
  V: maximum on width and summation on height
  H: maximum on height and summation on width
Bottom-up merging left and right subtrees
1
2
3
4
H1234
W1234
H
1
2
V
3
4
H
(d) Postfix expression: 12H34VH
W1234 = max(W12 + W34)
H1234 = H12 + H34

## Slide 31: Implementation using Stack
Very similar to the parathesis checking problem
Modification
  V/H: pack the top-two blocks (subtrees) vertically/horizontally
https://www.geeksforgeeks.org/check-for-balanced-parentheses-in-an-expression/

## Slide 32: How can We Handle Non-Slicing Tree?
Extend NEP to include pre-defined non-slicing block
a
b
c
d
e
f
g
h
i
H
H
H
H
V
W
h
i
c
d
e
f
g
a
b
H
H
Horizontal division (objects to the top and bottom)
H
V
Vertical division (objects to the left and right)
H
W
Wheel (4 objects cycled around a center object)

## Slide 33: Summary
Floorplan problem is NP hard (difficult to solve efficiently)
How to represent it compactly is a big deal
  Slicing is easier to deal with, so let’s start with it
  Next lectures will cover other representations
Polish expression is an elegant slicing-tree representation
  Need to be unique (NPE) to remove redundant space
  Can be implemented efficient using linear-time data structure
Simulated annealing algorithm fits well to floorplan
  Optimize the floorplan area and wirelength simultaneously