## Slide 1: Lecture 5: Circuit Partitioning – III
Tsung-Wei (TW) Huang
Department of Electrical and Computer Engineering
University of Utah, Salt Lake City, UT

## Slide 2: Circuit Partition
An essential step for reducing algorithm design complexity
  Divide and conquer (D&C)
Input
  A circuit graph
Output
  A set of partitioned subgraphs
Objective
  Minimize cross-connection

## Slide 3: KL Algorithm: Recap
1. Pair-wise exchange of nodes to reduce cut size
2. Allow cut size to increase temporarily within a pass
3. Compute the gain of a swap
Repeat
Perform a feasible swap of max gain
Mark swapped nodes “locked”
Update swap gains
Until no feasible swap
4. Find max prefix partial sum in gain sequence g1, g2, …, gm
5. Make corresponding swaps permanent
6. Start another pass if current pass reduces the cut size
u 
v 
v 
u 
locked

## Slide 4: FM Algorithm: Recap
Moves are made based on object gain – extended from KL algorithms
Object Gain: The amount of change in cut crossings that will occur if an object is moved from its current partition into the other partition
A pass description
While there is unlocked object
1. Each object is assigned a gain
2. Objects are put into a sorted gain list
3. The object with the highest gain from the larger of the two sides is selected and moved
4. The moved object is "locked"
5. Gains of "touched" objects are recomputed
6. Gain lists are resorted
Repeat the pass until there is no improvement

## Slide 5: State Space Search Problem
Combinatorial optimization problems (like partitioning) can be thought as a State Space Search Problem
A State is just a configuration of the combinatorial objects involved
The State Space is the set of all possible states (configurations)
A Neighborhood Structure is also defined (which states can one go in one step)
There is a cost corresponding to each state
Search for the min (or max) cost state

## Slide 6: Greedy Algorithm
A very simple technique for State Space Search Problem
Start from any state
Always move to a neighbor with the min cost (assume minimization problem)
Stop when all neighbors have a higher cost than the current state

## Slide 7: Problem with Greedy Algorithm
Easily get stuck at local minimum
Will obtain non-optimal solutions
Optimal only for convex (or concave for maximization) functions

## Slide 8: Greedy Nature of KL and FM
KL and FM are almost greedy algorithms
Purely greedy if we consider a pass as a “move”
Cut Value
Partitions
Pass 1
Pass 2
A
B
B
A
Move

## Slide 9: Simulated Annealing (SA) Algorithm
Very general search technique
Try to avoid being trapped in local minimum by making probabilistic moves
Popularize as a heuristic for optimization by:
  Kirkpatrick, Gelatt and Vecchi, “Optimization by Simulated Annealing”, Science, 220(4598):498-516, May 1983

## Slide 10: Basic Ideas of SA
Inspired by the Annealing Process:
  The process of carefully cooling molten metals in order to obtain a good crystal structure
  First, metal is heated to a very high temperature
  Then slowly cooled
  By cooling at a proper rate, atoms will have an increased chance to regain proper crystal structure
Attaining a min cost state in simulated annealing is analogous to attaining a good crystal structure in annealing

## Slide 11: Basic Ideas of SA (cont’d)
Non-zero probability for “up-hill” moves.
Probability depends on
  magnitude of the “up-hill” movement
  total search time
△C = cost(S’) – cost(S)
T: Control parameter (temperature)
Annealing schedule: T = T0, T1, T2,…, where Ti = riT0, r <1.

## Slide 12: Things to Consider in SA
When solving a combinatorial problem, we have to decide:
  The state space
  The neighborhood structure
  The cost function
  The initial state
  The initial temperature
  The cooling schedule (how to change t)
  The freezing point

## Slide 13: SA Algorithm Pseudocode
1 begin
2 Get an initial solution S;
3 Get an initial temperature T > 0;
4 while not yet “frozen” do
5 for 1 i P do
6 Pick a random neighbor S’ of S;
7 △ cost(S’) – cost(S); /* down hill move */
8 if △ 0 then SS’ /* uphill move */
9 if △ > 0 then SS’ with probability;
10 TrT ; /* reduce temperature */
11 return S
12 end

## Slide 14: Common Cooling Schedules
Initial temperature, cooling schedule, and freezing point are usually experimentally determined
  Parameter tuning is very critical in getting a good SA result
Some common cooling schedules
  t = at, where a is typically around 0.95
  t = e-bt t, where b is typically around 0.7
  …

## Slide 15: Basic SA Algorithm Structure
Solution space
Neighborhood structure
Cost function
Annealing schedule

## Slide 16: SA-based Partitioning Algorithm
Kirkpatrick, Gelatt, and Vecchi, “Optimization by simulated annealing,” Science, May 1983.
Solution space: set of all partitioning solutions
Neighborhood structure: move one cell to another partition

## Slide 17: SA-based Partitioning Algorithm (cont’d)
Cost function: f = C + λB
  C: the solution cost as used before
  B: a measure of balance
  λ: a constant
Annealing schedule
  Tn = rnT0, r = 0.9
  At each temperature, either 1. There are 10 accepted moves/cell on the average, or 2. # of attempts = 100 * total # of cells.
  The system is “frozen” if very low acceptances at 3 consecutive temperatures

## Slide 18: Evaluation of SA-based Partitioning
An extensive empirical study of Simulated Annealing versus Iterative Improvement Approaches have been studied over the past decades
Conclusion: SA is a competitive approach, getting better solutions than KL for random graphs
Remarks:
  Netlists are not random graphs, but sparse graphs with local structure
  SA is too slow. So KL/FM variants are still most popular
  Multiple runs of KL/FM variants with random initial solutions may be preferable to SA

## Slide 19: The Use of Randomness
For any partitioning problem:
Suppose solutions are picked randomly
If |G|/|A| = r, Pr(at least 1 good in 5/r trials) = 1-(1-r)5/r
If |G|/|A| = 0.001, Pr(at least 1 good in 5000 trials) = 1-(1-0.001)5000 = 0.9933
G
All solutions (state space)
Good solutions
A

## Slide 20: Adding Randomness to KL/FM
In fact, # of good states are extremely few
  Therefore, r is extremely small
Need extremely long time if just picking states randomly
  Therefore, we can running KL/FM variants several times with random initial solutions
Cut Value
Good Initial States
Good States

## Slide 21: Tie-breaking Strategy
For each vertex, instead of having a gain bucket, a gain vector is used
Gain vector is a sequence of potential gain values corresponding to numbers of possible moves into the future
Therefore, rth entry looks r moves ahead
Time complexity is O(pr), where r is max # of look-ahead moves stored in gain vector
If ties still occur, some researchers observe that LIFO order improves solution quality

## Slide 22: Other Partitioning Approaches
KL/FM-SA Hybrid: Use KL/FM variant to find a good initial solution for SA, then improve that solution by SA at low temperature
Tabu Search
Genetic Algorithm
Spectral Methods (finding Eigenvectors)
Network Flows
Quadratic Programming
…

## Slide 23: Multilevel Partitioning Techniques

## Slide 24: Coarsening Phase
Edge coarsening
Hyperedge coarsening (HEC)
Modified hyperedge coarsening (MHEC)

## Slide 25: Uncoarsening Phase
Based on FM with two simplifications
  Limit number of passes to 2
  Early-Exit FM (FM-EE), stop each pass if k vertex moves do not improve the cut
HER (Hyperedge Refinement)
  Move a group of vertices between partitions so that an entire hyperedge is removed from the cut

## Slide 26: hMETIS Algorithm: A Mixed Strategy
https://course.ece.cmu.edu/~ee760/760docs/hMetisManual.pdf
hMETIS-EE20
  20 random initial partitions
  with 10 runs using HEC for coarsening
  with 10 runs using MHEC for coarsening
  FM-EE for refinement
hMETIS-FM20
  20 random initial partitions
  with 10 runs using HEC for coarsening
  with 10 runs using MHEC for coarsening
  FM for refinement

## Slide 27: Summary
We have discussed problems of greedy partitioning algorithms
We have discussed simulated annealing (SA) algorithm
We have discussed SA-based partitioning algorithm
We have discussed multi-level partitioning algorithms