## Slide 1: Lecture 19: Timing Analysis – I
Tsung-Wei (TW) Huang
Department of Electrical and Computer Engineering
University of Utah, Salt Lake City, UT

## Slide 2: In-class Presentation: 12/7
Circuit partition research presentation on 9/14 (in class)
  Shiju Lin, Jinwei Liu, and Martin D F Wong, "GAMER: GPU-accelerated Maze Routing", IEEE/ACM ICCAD, 2021
  Zizheng Guo, Feng Gu, and Yibo Lin, "GPU-Accelerated Rectilinear Steiner Tree Generation," IEEE/ACM ICCAD, 2022
  Siting Liu, Yuan Pu, Peiyu Liao, Hongzhong Wu, Rui Zhang, Zhitang Chen, Wenlong Lv, Yibo Lin, Bei Yu, "FastGR : Global Routing on CPU-GPU with Heterogeneous Task Graph Scheduler," IEEE TCAD, 2022.
Upload your pptx to https://github.com/tsung-wei-huang/ece5960-physical-design/issues/14 before presentation

## Slide 3: Programming Assignment #3: Routing
Goal: Implement a Steiner Tree Construction Algorithm
Pins to connect
Route it so we guarantee each 2-point path
is shortest;
Redraw it--different
orientations
of 2-point paths
Now we can see the
better (shorter)
Steiner tree
Due 12/16: https://github.com/tsung-wei-huang/ece5960-physical-design/tree/main/PA3

## Slide 4: Physical Design Flow
Combinational
Logic
(No feedback
loops)
Flip Flops
Flip Flops
Clock input constraint
(e.g., need to pass within 1 cycle
•
•
•
•
•
•

## Slide 5: Timing Analysis in Design Automation
Deep interactions between logic synthesis and layout
Important facts
  Logic-side tools estimate delays through unplaced/unrouted logic
  Layout tools estimate delays through placed/routed logic
High-level
description
+
Timing
Specifications
Logic
Synthesis
Physical
Design
Connected cells
with delay constraints
on signal paths
Placed cells
with real locations,
real connecting wires

## Slide 6: Logic-Side Timing Analysis
Logic-side: How do we estimate the worst-case timing through a logic network?

## Slide 7: Layout-Side Timing Analysis
Layout-side: We place the gates, route the wires: how do we estimate wire delays?
Logic-side: How do we estimate the worst-case timing through a logic network?

## Slide 8: Big Picture
On the logic side:
  All problems look like longest (or shortest) paths through a graph that properly models the gates, and (maybe) the wires
On the layout side:
  The problem starts as an electrical circuit model (this is unavoidable)
  However, we skip circuit details, and just show key results
Surprisingly, both problems can be easily and efficiently solved using shortest path algorithms!

## Slide 9: Timing Analysis at Logic Level
Goal: Verify timing behavior of our logic design
  I give you a gate-level netlist
  I give you some timing models of the gates and (after place/route) the wires too
  You tell me:
    When signals arrive at various points in the network
    Longest delays through gate network
    Does the netlist satisfy the timing requirement? If not – where are key problems?
Challenge: How do you estimate the timing correctly?
  We can’t! But we know the worst and best-case timing

## Slide 10: Analyze Design Performance
Practical designs are synchronous
  All storage is in explicit sequential elements, e.g., flip-flop elements
  We can just focus on delays through combinations gates
Combinational
Logic
(No feedback
loops)
Flip Flops
Flip Flops
Common
Clock
•
•
•
•
•
•

## Slide 11: Can’t We Just Simulate Logic?
What logic simulation does
  Determine how a system will behave, simulates the logical function
  Gives the most accurate answer (with good simulation models)
  … but it is (practically) impossible to give a complete answer – especially timing
Requires examination of an exponential number of cases
  All possible input vectors …
  With all possible relative timings …
  Under all possible manufacturing variations …
We need a different, faster solution

## Slide 12: Timing Analysis: Basic Model
Assume we know clock cycle: e.g., 1GHz clock, cycle = 1ns
Logic
Flip Flops
Flip Flops
•
•
•
•
•
•
Longest delay <1ns
1 ns
CLOCK
For this logic to work successfully, longest delay through network must be shorter than 1ns
(For simplicity, ignore some flip flop timing issues)

## Slide 13: Timing Analysis: Basic Model (cont’d)
We need a model of delay through each logic gate
network delay == ?
Gate delay ∆ == ?
∆

## Slide 14: In the Real World …
Gate type affects delay
∆
∆
≠
Gate loading affects delay
∆
∆
≠
Waveform shape affects delay
∆
∆
≠
Transition direction affects delay
∆
∆
≠

## Slide 15: In the Real World … (cont’d)
Gate input pin affects delay
∆
≠
∆
At nanoscale, delays are really statistical
∆
∆
≠
http://upload.wikimedia.org/wikipedia/commons/8/8c/Standard_deviation_diagram.svg

## Slide 16: Our Model: Pin-to-Pin Delay
We will keep it simple: Fixed, pin-to-pin delay model
  No slopes, electricity, distributions, etc. – Just gate delay itself!
  Per-pin delays are essential, but we’ll use just 1 value per gate
  Turns out this is enough to see all the interesting algorithm ideas
∆=3
∆=3
∆=4.1
∆=4.1

## Slide 17: Example
PI = Primary Input, PO = Primary Output
∆=8
∆=1
∆=2
∆=8
∆=1
∆=2
∆=1
PI
PI
PI
PO
∆ = Gate delay
Notes: Let’s take a look at an example. Here, I have a simple graph model of three inputs, PI, and one output, PO, and seven gates. Each of the 7 gates has a delay value denoted by the delta. (explain …)
Now, based on this graph model. The job of timing analysis is to answer the questions “what is the longest path that gives the most delay?”

## Slide 18: Example (cont’d)
PI = Primary Input, PO = Primary Output
∆=8
∆=1
∆=2
∆=8
∆=1
∆=2
∆=1
PI
PI
PI
PO
Longest delay is 8+2+8+2=20

## Slide 19: Static Timing Analysis (STA)
When we ignore logic, this is called Topological Analysis
  We only work with the graph and the delays – don’t consider the logic
  We can get wrong answers: what we found was called a False Path
Going forward: we ignore the logic
  Assume that all paths are statically sensitizable
    Means: Can find a constant pattern of inputs to other PIs that makes some output sensitive to some input
This timing analysis is called Static Timing Analysis (STA)
  Consider only the best- and worst-case timing results
  Consider no logic (otherwise called dynamic timing analysis)
Notes: Now, you probably can see, in this type of analysis, we only consider gate delay and do not consider the functionality of the circuit or the logic of the circuit. Evenything is done in an abstract graph model. When we ignore logic … (explain…)

## Slide 20: STA Representation: Delay Graph
From gate-level network, we build a delay graph
  Vertices: Wires in gate network, 1 per gate output, 1 for each PI and PO
  Edges: Gates, input pin to output pin (1 edge per input). Put gate delays on edges
PI=a
PI=b
c
PI=d
e=PO
∆=2
∆=2
∆=3
∆=3
d
c
a
b
e
2
2
3
3
Called Cell arcs. Because they are edges, that explain timing, for each cell in tech library.

## Slide 21: Source and Sink in Delay Graph
Common convention: Add Source / Sink nodes
  Add 1 “source” (SRC) node that has a 0-weight edge to each PI
  Add1 “sink” (SNK) node with 0-weight edge from each PO
  Why do this?
    Now, the network has exactly 1 “entry” node, and 1 “exit” node
    All the longest (or shortest) path question have same start / end nodes
a
d
c
b
e
2
2
3
3
SNK
0
SRC
0
0
0

## Slide 22: What about Interconnect among Gates?
Can still use delay graph: model each wire as a “special” gate that just has a delay
PI=a
PI=b
c
PI=d
e
x
y
w
z
q=PO
∆=2
∆=3
∆=1.2
∆=1.6
∆=1.5
∆=1.0
∆=1.8
a
d
c
b
e
x
y
w
z
q
SRC
0
0
SNK
0
0
1.2
1.6
2
2
1.5
1.0
3
1.8
3

## Slide 23: Operations on Delay Graph
So how do we use this graph to do timing analysis?
  What we do not do: Try to enumerate all the source-to-sink paths
  Why not? Exponential explosion in number of paths, even for small graph
There’s a smarter answer: Node-oriented timing analysis
  Find, for each node in delay graph, worst delay to the node along any path
0
1
2
3
n
• • •
How many paths from 1 to n? 2n !

## Slide 24: Define Values on Nodes in Delay Graph
SRC
SNK
n
other paths
ATs
RATs
Arrival Time at a node (AT)
  AT(n) = Latest time the signal can become stable node n
  Think: Longest path from source
  Called: Delays TO node
Required Arrival Time at node (RAT)
  RAT(n)=Latest time the signal is allowed to become stable at node n
  Think: Longest path to sink (sort of…)
  Called: Delays FROM node

## Slide 25: Measure Timing Margin at a Node
Slack at node n: Slack(n) = RAT(n) – AT(n)
  Amount of timing “margin” for the signal: positive is good, negative is bad
  Determined by longest path through node
  Amount by which a signal can be delayed at node and not increase the longest path through the network
  Can increase delay at node (to minimize power, circuit area) with positive slack and not degrade overall performance
SRC
SNK
n
other paths
ATs
RATs
  Slack(n) = RAT(n) - AT(n)

## Slide 26: Slack is Important in Timing Analysis
About slacks
  Defined so negative slack always bad --, it indicates a timing problem
  Measures “sensitivity” of network to this node’s delay
Positive slack
  Good: I can change something at this node, and not hurt network’s overall timing
  Example: I can make this node slower, maybe save some power, not hurt timing
Negative slack
  Bad: I have problem at this node; more negative the slack, bigger the problem
  Looking for a node to “fix” to help timing? These nodes are where to look first. These affect my critical paths the most

## Slide 27: How to Compute Arrival Time (AT)?
succ(n)
successor paths
SRC
SNK
n
-
p
-
-
s
-
•
•
•
•
•
•
∆(p,n)
pred(n)
predecessors of n
predecessor
paths
AT(n) = maximum delay to n =
0 if n == SRC
MAX AT(p) + ∆(p,n) else
p ∊ pred(n)
AT can be computed Recursively!

## Slide 28: Example: Compute AT
If we know the longest path to each predecessor of n, it’s a simple “Maximum” operation to compute the longest path to n itself—Yes, it is shortest-path algorithm again!
MAX { AT(x) + ∆(x,n) }
x∈{p, q, r}
= MAX { 5+7, 10+1, 5+5 }
= 10
n
p
q
r
SRC
• • •
• • •
• • •
∆=7
AT(p) =5
∆=1
AT(q)=10
∆=5
AT(r)=5
AT(n) =

## Slide 29: How to Compute Required Arrival Time (RAT)?
pred(n)
predecessor
paths
SRC
SNK
n
-
p
-
-
s
-
•
•
•
•
•
•
∆(n,s)
succ(n): successors of n
successor paths
RAT(n) =
Latest time in cycle
where n could change and signal would still propagate to sink before end of cycle
Cycle Time if n == SNK
MIN RAT(s) - ∆(n,s) else
s ∊ succ(n)
=
Cycle Time
CLOCK
RATs are defined relative to clock cycle

## Slide 30: ATs vs RATs: Look at the Clock Cycle
Cycle Time if n == SNK
MIN RAT(s) - ∆(n,s) else
s ∊ succ(n)
0 if n == SRC
MAX AT(p) + ∆(p,n) else
p ∊ pred(n)
AT(n)
RAT(n)
AT(n)
AT: longest logic delay after launch edge of clock
RAT(n)
RAT: longest logic delay to the capture edge of clock, but it is
expressed relative to the Cycle Time
Why the difference between ATs and RATs?

## Slide 31: Bad Things Happen When We See This
SLACK = RAT – AT = Negative
Signal arrives too late, and there is too much delay from node to output
Signal does not arrive at flip flip input before the capture edge of clock
AT(n)
RAT(n)
CLOCK: Cycle Time
Launch
Edge
Capture
Edge

## Slide 32: Let’s Do a Bigger Example
Delays are on edges; let clock cycle be 12
  Compute the min/max delays “by eye” for now
  AT=longest path from SRC TO node;
  RAT=(cycle time 12) – (longest path FROM node to SNK)
  Slack = RAT - AT
Cycle=12
1
4
1
2
3
5
2
3
1
5
3
2
4
SNK
SRC
0
0
0
0
0
0
PIs
POs

## Slide 33: Compute ATs …
1
4
1
2
3
5
2
3
1
5
3
2
4
SNK
SRC
0
0
0
0
0
0
PIs
POs
 AT RAT slackL = (RATL – ATL)
Compute ATs from SRC to SNK
0
0
0
0
6
1
2
4
10
12
7
15
15
Cycle=12

## Slide 34: Compute RATs …
1
4
1
2
3
5
2
3
1
5
3
2
4
SNK
SRC
0
0
0
0
0
0
PIs
POs
 AT RAT slackL = (RATL – ATL)
0
0
0
0
1
6
2
4
10
12
7
15
15
Compute RATs from SNK to SRC
12
12
12
12
10
7
3
-2
4
-3
-1
2
-3
Cycle=12

## Slide 35: Compute Slacks …
1
4
1
2
3
5
2
3
1
5
3
2
4
SNK
SRC
0
0
0
0
0
0
PIs
POs
 AT RAT slackL = (RATL – ATL)
0
0
0
0
1
6
2
4
10
12
7
15
15
12
12
12
12
10
7
3
-2
4
-3
-1
2
-3
-3
-3
-1
2
-3
2
-3
6
-3
5
0
-3
-3
Worst (most negative slack) is -3. Trace worst path, SRCSNK
Cycle=12

## Slide 36: Debrief
Look at those slacks
  A negative slack at an output (PO) means a missed requirement
  A negative slack on internal node n means it feeds a problem PO
    So, there is a path from n to some problem PO
Key: negative slack appears along this entire worst path
  Your worst timing violation at an output (PO) = the most negative slack value
  You can always trace a path with this slack value back to a PI
So, slacks are hugely useful
  Beyond just knowing what is the worst path; slacks tell us problem gates on this path

## Slide 37: Summary – Happy Thanksgiving!
We have discussed the timing analysis problem
We have discussed the static timing analysis (STA) model
We have discussed computational models to STA
We have discussed measurement of STA results